## Slide 1: Unit 01.01.01 CS 5220: COMPUTER COMMUNICATIONS
Evolution of Communication Networks
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: What is a Communication Network?
The equipment (hardware & software) and facilities that provide the basic communication service
Communication
Network
Equipment
  Routers, servers, switches, …
Facilities
  Copper wires, optical fiber …

## Slide 3: Network Architecture Evolution
Telegraph
networks
Telephone
networks
Internet, Optical
& Wireless
networks
Information transfer
per second
Next Generation Internet
?

## Slide 4: Telegraph Networks
Telegraph: a message is transmitted across a network using signals
  Drums, beacons, mirrors, smoke, flags, semaphores…
  Electricity, light

## Slide 5: Digital Communications
Morse code converts text message in sequence of dots & dashes
Use transmission system designed to convey dots and dashes
 | Morse Code |  | Morse Code |  | Morse Code |  | Morse Code
A | · — | J | · — — — | S | · · · | 2 | · · — — —
B | — · · · | K | — · — | T | — | 3 | · · · — —
C | — · — · | L | · — · · | U | · · — | 4 | · · · · —
D | — · · | M | — — | V | · · · — | 5 | · · · · ·
E | · | N | — · | W | · — — | 6 | — · · · ·
F | · · — · | O | — — — | X | — · · — | 7 | — — · · ·
G | — — · | P | · — — · | Y | — · — — | 8 | — — — · ·
H | · · · · | Q | — — · — | Z | — — · · | 9 | — — — — ·
I | · · | R | · — · | 1 | · — — — — | 0 | — — — — —

## Slide 6: Electric Telegraph Networks
Switches
Message
Destination
Source
Message
Message
Message
Electric telegraph networks exploded
  Message switching & Store-and-Forward operation
  Key elements: Framing, Multiplexing, Addressing, Routing, Forwarding

## Slide 7: Elements of Telegraph Networks
Digital transmission
  Text messages converted into symbols
  Transmission system designed to convey symbols
Multiplexing
  Framing needed to recover text characters
Message Switching
  Messages contain source & destination addresses
  Store-and-Forward: messages forwarded hop-by-hop across network
  Routing according to destination address

## Slide 8: Bell’s Telephone
Alexander G. Bell (1876) working on harmonic telegraph to multiplexing discovered voice signals can be transmitted directly
  Microphone converts voice pressure variation into analogous electrical signal
  Loudspeaker converts electrical signal back into sound
Basic telephone service involves two-way, real-time transmission of voice signals across a network
  Signaling required to establish a call
Signaling + voice signal transfer

## Slide 9: The N2 Problem
Initially, p2p direct communications - for N users to be fully connected directly
  Requires too much space for cables
  Inefficient & costly since connections not always on
N = 1000
N(N – 1)/2 = 499500
1
2
3
4
N
. . .

## Slide 10: Circuit Switching is Connection-oriented
Patchcord panel switch invented in 1878
Operators connect users on demand
  Establish circuit to allow electrical current to flow from inlet to outlet
Only N connections required to central office
1
2
3
N – 1
N

## Slide 11: Hierarchical Tele-Network Structure
Tandem
CO
Toll
CO
CO
CO
CO
Tandem
CO = central office
last mile
trunks
switching
End-to-end connection requires collaborative switching

## Slide 12: Elements of Telephone Networks
Digital transmission & switching
  Digital voice; Time Division Multiplexing
Circuit switching – Connection oriented
  User signals for call setup and tear-down
  Route selected during connection setup
  End-to-end connection across network
  Signaling coordinates connection setup
Hierarchical Network Structure
  Decimal numbering system
  Hierarchical structure; simplified routing; scalability

## Slide 13: Network Architecture Evolution
Telegraph Networks
  Message switching & store-and-forward
Telephone Networks
  Circuit Switching and connection oriented
Computer Networks and the Internet
  Packet switching
  Virtual circuit switching
Next-Generation Internet
  ???

## Slide 14: Summary of the Lesson
History often repeats itself

## Slide 15: Unit 01.01.02 CS 5220: COMPUTER COMMUNICATIONS
Computer Network Evolution
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 16: Computer Network Evolution
1960s: Terminals access shared host computer
  SAGE; SABRE airline reservation system
  Tree-topology terminal-oriented networks
1970s: Computers connect directly to each other
  ARPANET packet switching network
  TCP/IP Internet protocols
  Ethernet local area network
1980s - 2000s: New applications and Internet growth
  Commercialization of Internet
  E-mail, file transfer, web, P2P, . . .
  Internet traffic surpasses voice traffic

## Slide 17: Terminal-Oriented Networks
Early computer systems very expensive; Time-sharing methods allowed multiple terminals to share local computer
Remote access via telephone modems
Host computer
Terminal
Terminal
. . .
Terminal
Modem
Modem
Telephone
Network

## Slide 18: Medium Access Control
Dedicated communication lines were expensive
Terminals generated messages sporadically
Frames carried messages to/from attached terminals
Address in frame header identified terminal
Medium Access Controls for sharing a line in arbitrated manner
Example: Polling protocol on a multi-drop line
Terminal
Terminal
. . .
Terminal
Polling frames & output frames
input frames

## Slide 19: Multiplexing
Multiplexer allows a line to carry frames to/from multiple terminals
Frames are buffered at multiplexer until line becomes available, i.e. store-and-forward
Header carries other control information for framing
CRC Information Header
Header Information CRC
Host computer
Terminal
Terminal
. . .
Terminal
Multiplexer
Frame

## Slide 20: Error Control Protocol
Communication lines introduced errors
Error checking codes used on frames
  “Cyclic Redundancy Check” (CRC) calculated based on frame header and information payload, and appended
  Header also carries ACK/NAK control information
Retransmission requested when errors detected
Header Information CRC
CRC Information Header
Terminal

## Slide 21: Computer-to-Computer Networks
As cost of computing dropped, terminal-oriented networks viewed as too inflexible and costly
Need to develop flexible computer networks
  Interconnect computers as required
  Support many applications
Application Examples
  File transfer between arbitrary computers
  Execution of a program on another computer

## Slide 22: Packet Switching
Network should support multiple applications
  Transfer arbitrary message size
  Low delay for interactive applications
  Store-and-forward operation could induce high delay on interactive messages
Packet switching introduced
  Network transfers packets using store-and-forward
  Packets have maximum length
  Break long messages into multiple packets
  By switching, packets delivered (and reassembled) at destination

## Slide 23: The ARPANET
The vulnerability of the telephone system was a concern.
(a) Telephone system structure; (b) Distributed switching system structure

## Slide 24: The ARPANET Design
Connection-less packet transmission
Packets are encapsulated in frames
Error control uses check bits
Destinations identified by unique addresses
Routing tables at the packet switches
Messages are segmented into packets
End-to-end congestion control
Flow control prevents buffer overflow

## Slide 25: ARPANET Applications
ARPANET (NSF-NET) introduced new applications
  Email, remote login, file transfer, …
UCLA
RAND
TINKER
USC
NBS
UCSB
HARV
SCD
BBN
STAN
AMES
AMES
McCLELLAN
UTAH
BOULDER
GWC
CASE
CARN
MITRE
ETAC
MIT
ILL
LINC
RADC

## Slide 26: Ethernet Local Area Network
In 1980s, affordable workstations available
Need for low-cost, low error rate, high-speed network, possible using coaxial cable
Broadcasting, medium access control
Network interface card with a unique address
Ethernet is the standard for high-speed wired access to computer networks

## Slide 27: Summary of the Lesson
Services and Applications drive network architecture design

## Slide 28: Unit 01.01.03 CS 5220: COMPUTER COMMUNICATIONS
Examples of Protocols and Services
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 29: Services & Applications
Service: information transfer capability
  Internet transfer of individual block of information
  Internet reliable transfer of a stream of bytes
  Real-time transfer of a voice signal
Applications build on communication services
  E-mail & web build on reliable stream service
New applications build on multiple networks
  SMS builds on Internet reliable stream service and cellular telephone text messaging

## Slide 30: Layers, Services & Protocols
The overall communications process between machines connected across one or more networks is very complex
Layering partitions related communications functions into groups that are manageable
Each layer provides a service to the layer above
Each layer operates according to a protocol

## Slide 31: DNS
User clicks on http://www.nytimes.com/
URL contains Internet name of machine (www.nytimes.com), but not Internet address
Internet needs Internet address to send information to a machine
Browser software uses Domain Name System (DNS) protocol to send query for Internet address
DNS system responds with Internet address
Q. www.nytimes.com?
A. 64.15.247.200

## Slide 32: 2. TCP
Browser software uses HTTP to send request for document
HTTP server waits for requests by listening to a well-known port number (80 for HTTP)
HTTP client sends request messages through an “ephemeral port number,” e.g. 1127
HTTP needs a Transmission Control Protocol (TCP) connection between the HTTP client and HTTP server to transfer messages reliably
TCP Connection Request
From: 128.100.11.13 Port 1127
To: 64.15.247.200 Port 80
ACK, TCP Connection Request
From: 64.15.247.200 Port 80 To:128.100.11.13 Port 1127
ACK

## Slide 33: 3. HTTP
HTTP client sends its request message: “GET comm.html …”
HTTP server sends a status response: “200 OK”
HTTP server sends requested file
Browser displays document
Clicking a link sets off a chain of events across the Internet!
GET / HTTP/1.1
200 OK
Content

## Slide 34: Protocols
A protocol is a set of precise & unambiguous rules that governs
  how two or more communicating entities in a layer are to interact
  Messages that can be sent and received
  Actions that are to be taken when a certain event occurs
The purpose of a protocol is to provide a service to the layer above

## Slide 35: Example: HTTP
HTTP is an application layer protocol
Retrieves documents on behalf of a browser application program
HTTP specifies fields in request messages and response messages
  Request types; Response codes
  Content type, options, cookies, …
HTTP specifies actions to be taken upon receipt of certain messages

## Slide 36: HTTP uses service of TCP
HTTP
server
HTTP
client
Port 80
Port 1127
GET
TCP
TCP

## Slide 37: HTTP uses service of TCP - CONT
HTTP
server
HTTP
client
Port 80
Port 1127
TCP
TCP
TCP
80, 1127
GET

## Slide 38: HTTP uses service of TCP- CONT
HTTP
server
HTTP
client
Port 80
Port 1127
GET
TCP
TCP

## Slide 39: HTTP uses service of TCP- CONT
HTTP
HTTP
client
Port 80
Port 1127
GET
TCP
TCP
RESPONSE

## Slide 40: HTTP uses service of TCP- CONT
HTTP
HTTP
client
Port 80
Port 1127
TCP
TCP
1127, 80
RESPONSE

## Slide 41: HTTP uses service of TCP- CONT
HTTP
HTTP
client
Port 80
Port 1127
GET
TCP
RESPONSE

## Slide 42: Example: DNS Protocol
DNS protocol is an application layer protocol
DNS is a distributed database that resides in multiple machines in the Internet
DNS protocol allows queries of different types
DNS usually involves short messages and so uses service provided by UDP
Well-known port 53

## Slide 43
Local Name Server: resolve frequently-used names
  E.g., University department, ISP
Root Zone Name Servers
  Resolves query or refers query to Authoritative Name Server
Authoritative Name Server: last resort, 13 autoorities
  Every machine must register its address with at least two servers
1
2
3
4
5
6
Local
Name
Server
Root
Name
Server
Authoritative
Name
Server

## Slide 44: Summary
Services: a protocol provides a communications service to the layer above
DNS servers are one primary target of cyber attacks