## Slide 1: Unit 01.03.01 CS 5220: COMPUTER COMMUNICATIONS
Berkeley Socket API - I
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Berkeley Socket API
Berkeley UNIX Sockets API
  Abstraction for applications to send & receive data
  Applications create sockets that “plug into” network
  Applications write/read to/from sockets
  Implemented in the kernel
  Facilitates development of network applications
  Hides details of underlying protocols & mechanisms
Also in Windows, Linux, and other OS’s

## Slide 3: Communications through Sockets
Client
Server
descriptor
port number
descriptor
port number
Application references a
socket through a descriptor
Socket bound to a port number
Application 1
Socket
Socket interface
User
Kernel
Application 2
User
Kernel
Underlying communication protocols
Underlying communication protocols
Communications network
Socket
Socket interface

## Slide 4: Transport Protocols
Host computers run two transport protocols on top of IP to enable process-to-process communications
User Datagram Protocol (UDP) enables best-effort connectionless transfer of individual block of information
Transmission Control Protocol (TCP) enables connection-oriented reliable transfer of a stream of bytes
Two services though Sockets: connection-oriented and connection-less

## Slide 5: Stream Mode of Service
Connection-oriented (TCP)
First, setup connection between two peer application processes
Then, reliable bidirectional in-sequence transfer of byte stream (boundaries not preserved in transfer)
Multiple write/read between peer processes
Finally, connection release
Connectionless (UDP)
Immediate transfer of one block of information (boundaries preserved)
No setup overhead & delay
Destination address with each block
Send to/receive from multiple peer processes
Best-effort service only
  Possible out-of-order
  Possible loss

## Slide 6: Client & Server Differences
Server
  Specifies well-known port # when creating socket
  May have multiple IP addresses (net interfaces)
  Waits passively for client requests
Client
  Assigned ephemeral port #
  Initiates communications with server
  Needs to know server’s IP address & port #
    DNS for URL & server well-known port #
  Server learns client’s address & port #

## Slide 7: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
close()
Server does Passive Open
socket call creates socket to listen for connection requests
Server specifies type: TCP (stream)
socket call returns: non-negative integer descriptor; or -1 if unsuccessful

## Slide 8: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
bind assigns local address & port # to socket with specified descriptor
Can wildcard IP address for multiple net interfaces
bind call returns: 0 (success); or -1 (failure)
Failure if port # already in use or if reuse option not set
close()

## Slide 9: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
listen indicates to TCP readiness to receive connection requests for socket with given descriptor
Parameter specifies max number of requests that may be queued while waiting for server to accept them
listen call returns: 0 (success); or -1 (failure)
close()

## Slide 10
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Server calls accept to accept incoming requests
accept blocks if queue is empty
close()

## Slide 11: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
close()
Client does Active Open
socket call creates socket to connect to server
Client specifies type: TCP (stream)
socket call returns: non-negative integer descriptor; or -1 if unsuccessful

## Slide 12
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
close()
connect establishes a connection on the local socket with the specified descriptor to the specified remote address and port #
connect returns 0 if successful; -1 if unsuccessful
Note: connect initiates TCP three-way handshake

## Slide 13: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
accept wakes with incoming connection request
accept fills client address & port # into address structure
accept call returns: descriptor of new connection socket (success); or -1 (failure)
Client & server use new socket for data transfer
Original socket continues to listen for new requests
close()
Socket Calls for Connection-Oriented Mode

## Slide 14
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Data Transfer
Client or server call write to transmit data into a connected socket
write call returns: # bytes transferred (success); or -1 (failure); blocks until all data transferred
close()

## Slide 15
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Data Transfer
Client or server call read to receive data from a connected socket
read specifies: socket descriptor; pointer to a buffer; amount of data
read call returns: # bytes read (success); or -1 (failure); blocks if no data arrives
close()
Note: write and read can be called multiple times to transfer byte streams in both directions

## Slide 16
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Connection Termination
Client or server call close when socket is no longer needed
close specifies the socket descriptor
close call returns: 0 (success); or -1 (failure)
Note: close initiates TCP graceful close sequence
close()
Socket Calls for Connection-Oriented Mode

## Slide 17: Summary of the Lesson
  Socket API hides details of underlying protocols & mechanisms

## Slide 18: Unit 01.03.02 CS 5220: COMPUTER COMMUNICATIONS
Berkeley Socket API - II
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 19: Stream Mode of Service
Connectionless (UDP)
Immediate transfer of one block of information (boundaries preserved)
No setup overhead & delay
Destination address with each block
Send/receive to/from multiple peer processes
Best-effort service only
  Possible out-of-order
  Possible loss

## Slide 20: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
Server starts first
Socket call creates socket of type UDP (datagram)
socket call returns: descriptor; or -1 if unsuccessful
bind assigns local address & port # to socket with specified descriptor

## Slide 21: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
recvfrom copies bytes received in specified socket into a specified location
recvfrom blocks until data arrives

## Slide 22: Socket Calls for Connection-Less Mode
sendto()
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
Client started
socket creates socket of type UDP (datagram)
socket call returns: descriptor; or -1 if unsuccessful

## Slide 23
sendto()
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto transfer bytes in buffer to specified socket
sendto specifies: socket descriptor; pointer to a buffer; amount of data; flags to control transmission behavior; destination address & port #; length of destination address structure
sendto returns: # bytes sent; or -1 if unsuccessful

## Slide 24
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
recvfrom wakes when data arrives
recvfrom specifies: socket descriptor; pointer to a buffer to put data; max # bytes to put in buffer; control flags; copies: sender address & port #; length of sender address structure
recvfrom returns # bytes received or -1 (failure)
Note: recvfrom returns data from at most one send, i.e. from one datagram

## Slide 25: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
Socket Close
Client or server call close when socket is no longer needed
close specifies the socket descriptor
close call returns: 0 (success); or -1 (failure)

## Slide 26: Example-I: TCP Echo Server
As illustration of the use of system calls and functions, let’s see two programs communicate via TCP.
The client prompts a user to type a line of text and sends it to the server, and reads the data back from the server.
The server aces as a simple each server.
In this example, each program expects a fixed number of bytes from the other end, defined by BUFLEN.
The example code is given in the Textbook Chapter 2.4

## Slide 27: TCP Echo Server - Binding
/* Bind an address to the socket */
bzero((char *)&server, sizeof(struct sockaddr_in));
server.sin_family = AF_INET;
server.sin_port = htons(port);
server.sin_addr.s_addr = htonl(INADDR_ANY);
if (bind(sd, (struct sockaddr *)&server,
sizeof(server)) == -1) {
fprintf(stderr, "Can't bind name to socket\n");
exit(1);
}

## Slide 28: TCP Echo Server - Connections
/* queue up to 5 connect requests */
listen(sd, 5);
while (1) {
client_len = sizeof(client);
if ((new_sd = accept(sd, (struct sockaddr *)&client, &client_len)) == -1) {
fprintf(stderr, "Can't accept client\n");
exit(1);
}

## Slide 29: TCP Echo Server – Repeated Byte Reads
/* Repeated calls to read until all data received */
bp = buf;
bytes_to_read = BUFLEN;
while ((n = read(new_sd, bp, bytes_to_read)) > 0) {
bp += n;
bytes_to_read -= n;
}
printf("Rec'd: %s\n", buf);
write(new_sd, buf, BUFLEN);
printf("Sent: %s\n", buf);
close(new_sd);

## Slide 30: TCP Echo Client – Name-to-Address
bzero((char *)&server, sizeof(struct sockaddr_in));
server.sin_family = AF_INET;
server.sin_port = htons(port);
if ((hp = gethostbyname(host)) == NULL) {
fprintf(stderr, "Can't get server's address\n");
exit(1);
}
bcopy(hp->h_addr, (char *)&server.sin_addr, hp->h_length);

## Slide 31: TCP Echo Client - Connection
/* Connecting to the server */
if (connect(sd, (struct sockaddr *) &server, sizeof(server)) == -1) {
fprintf(stderr, "Can't connect\n");
exit(1);
}
printf("Connected: server's address is %s\n", hp->h_name);

## Slide 32: TCP Echo Client – Repeated reads
printf("Receive:\n");
bp = rbuf;
bytes_to_read = BUFLEN;
while ((n = read(sd, bp, bytes_to_read)) > 0) {
bp += n;
bytes_to_read -= n;
}
printf("%s\n", rbuf);

## Slide 33: Example-II: UDP Echo Server
while (1) {
client_len = sizeof(client);
if ((n = recvfrom(sd, buf, MAXLEN, 0, (struct sockaddr *)&client, &client_len)) < 0) {
fprintf(stderr, "Can't receive datagram\n"); exit(1);
}
if (sendto(sd, buf, n, 0, (struct sockaddr *)&client, client_len) != n) {
fprintf(stderr, "Can't send datagram\n");
exit(1);
}
}

## Slide 34: Example: UDP Echo Client
gettimeofday(&start, NULL); /*start delay measurement*/
server_len = sizeof(server);
if (sendto(sd, sbuf, data_size, 0, (struct sockaddr *)
&server, server_len) == -1) {
fprintf(stderr, "sendto error\n")
exit(1);
}
if (recvfrom(sd, rbuf, MAXLEN, 0, (struct sockaddr *)
&server, &server_len) < 0) {
fprintf(stderr, "recvfrom error\n");
exit(1);
}
gettimeofday(&end, NULL); /* end delay measurement */

## Slide 35: Summary: UDP Rliability
As UDP is unreliable, users may have to take care of reliability assurance by themselves.
LAN vs. WAN
Timeout mechanism avoids forever wait
Re-transmission to get a lost message
Reordering and de-duplication are requiired for reliability

## Slide 36: Unit 01.03.03 CS 5220: COMPUTER COMMUNICATIONS
Digital Communication Fundamentals
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 37: Interests of Interest
How long will it take to transmit a message?
  How many bits are in the message (text, image)?
  How fast does the network/system transfer information?
Can a network/system handle a voice (video) call?
  How many bits/second does voice/video require?
How long will it take to transmit a message?
What transmission speed is possible over radio, copper cables, fiber, …?

## Slide 38: Bits, numbers, information
Bit: number with value 0 or 1
  n bits: digital representation for 0, 1, … , 2n
  Byte or Octet, n = 8
  Computer word, n = 16, 32, or 64
n bits allows enumeration of 2n possibilities
  n-bit field in a header
  n-bit representation of a voice sample
  Message consisting of n bits
The number of bits required to represent a message is a measure of its information content; more bits means more content

## Slide 39: Block vs. Stream Information
Block
Information that occurs in a single block
  Text message
  Data file
  JPEG image
Size = Bits / block
or bytes/block
  1 kbyte = 210 bytes
  1 Mbyte = 220 bytes
  1 Gbyte = 230 bytes
Stream
Information that is produced & transmitted continuously
  Real-time voice
  Streaming video
Bit rate = bits / second
  1 kbps = 103 bps
  1 Mbps = 106 bps
  1 Gbps =109 bps

## Slide 40: Delay – Propagation Delay
tprop time for signal to propagate across medium
d distance between two nodes in meters
v speed of light in the transmission medium (3x108 m/s in vacuum)
The delay of communication between two nodes has two components, the propagation delay and the transmission delay
The propagation delay tprop = d/v

## Slide 41: Delay - Transmission Delay
Use data compression to reduce L
Use higher bandwidth modem to increase R
Place server closer to reduce d
L number of bits in message
R bandwidth of digital transmission system in bps
The transmission delay: ttrans = L/R
Overall Delay = tprop + ttrans = d/v + L/R

## Slide 42: Compression
Information usually not represented efficiently
Data compression algorithms
  Represent the information using fewer bits
  Noiseless: original information recovered exactly
    E.g. zip, compress, GIF, fax
  Noisy: recover information approximately
    E.g., JPEG
    Tradeoff: # bits vs. quality
Compression Ratio
  #bits (original file) / #bits (compressed file)

## Slide 43: Examples of Block Information
Type | Method | Format | Original | Compressed(Ratio)
Text | Zip, compress | ASCII | Kbytes- Mbytes | (2-6)
Fax | CCITT Group 3 | A4 page 200x100 pixels/in2 | 256 kbytes | 5-54 kbytes (5-50)
Color Image | JPEG | 8x10 in2 photo 4002 pixels/in2 | 38.4 Mbytes | 1-8 Mbytes (5-30)

## Slide 44: Examples of Digital Video Signals
Type | Method | Format | Original | Compressed
Video Conference | H.261 | 176x144 or 352x288 pix @10-30 fr/sec | 2-36 Mbps | 64-1544 kbps
Full Motion | MPEG2 | 720x480 pix @30 fr/sec | 249 Mbps | 2-6 Mbps
HDTV | MPEG2 | 1920x1080 @30 fr/sec | 1.6 Gbps | 19-38 Mbps

## Slide 45: Trans. of Stream Information
Constant bit-rate
  Signals such as digitized telephone voice produce a steady stream: e.g. 64 kbps
  Network must support steady transfer of signal, e.g. 64 kbps circuit
Variable bit-rate
  Signals such as digitized video produce a stream that varies in bit rate, e.g. according to motion and detail in a scene
  Network must support variable transfer rate of signal, e.g. packet switching or rate-smoothing with constant bit-rate circuit

## Slide 46: Stream Quality-of-Service (QoS) Issues
Network Transmission Impairments
Delay: Is information delivered in timely fashion?
Jitter: Is information delivered in sufficiently smooth fashion?
Loss: Is information delivered without loss? If loss occurs, is delivered signal quality acceptable?
Applications & application layer protocols developed to deal with these impairments

## Slide 47: A Transmission System
Transmitter
Converts information into signal suitable for transmission
Injects energy into communications medium or channel
  Telephone converts voice into electric current; Modem converts bits into tones
Receiver
Receives energy from medium
Converts received signal into form suitable for delivery to user
  Telephone converts current into voice; Modem converts tones into bits
Receiver
Communication channel
Transmitter

## Slide 48: Transmission Impairments
Communication Channel
Pair of copper wires
Coaxial cable
Radio
Light in optical fiber
Infrared
Transmission Impairments
Signal attenuation
Signal distortion
Spurious noise
Interference from other signals
Transmitted Signal
Received Signal
Receiver
Communication channel
Transmitter

## Slide 49: Digital Long-Distance Communications
Regenerator (repeater) recovers original data sequence and retransmits on next segment
Each regeneration is like the first time!
Can redesign so error probability is very small
Source
Destination
Regenerator
Transmission segment
Regenerator
. . .

## Slide 50: Twisted Pair
(a) Category 3 UTP (16 MHz). (b) Category 5 UTP (100 MHz).
A twisted pair consists of two insulated copper wires, typically about 1mm thick; twisted together to reduce the susceptibility to interference.
  More twists per cm leads to less crosstalk and better quality over longer distance

## Slide 51: Twisted Pair Bit Rates
Twisted pairs can provide high bit rates at short distances
Asymmetric Digital Subscriber Loop (ADSL)
  High-speed Internet Access
  Lower 3 kHz for voice
  Upper band for data
  64 kbps inbound
  640 kbps outbound
Much higher rates possible at shorter distances
  Strategy for telephone companies is to bring fiber close to home & then twisted pair
Data rates of 24-gauge twisted pair
Standard | Data Rate | Distance
T-1 | 1.544 Mbps | 18,000 feet, 5.5 km
DS2 | 6.312 Mbps | 12,000 feet, 3.7 km
1/4 STS-1 | 12.960 Mbps | 4500 feet, 1.4 km
1/2 STS-1 | 25.920 Mbps | 3000 feet, 0.9 km
STS-1 | 51.840 Mbps | 1000 feet, 300 m

## Slide 52: Ethernet LANs
Category 3 unshielded twisted pair (UTP): ordinary telephone wires
Category 5 UTP: tighter twisting to improve signal quality
Shielded twisted pair (STP): to minimize interference; costly
10BASE-T Ethernet
  10 Mbps, Baseband, Twisted pair
  Two Cat3 pairs
  Manchester coding, 100 meters
100BASE-T4 Fast Ethernet
  100 Mbps, Baseband, Twisted pair
  Four Cat3 pairs
  Three pairs for one direction at-a-time
  100/3 Mbps per pair;
  3B6T line code, 100 meters
Cat5 & STP provide other options
     

## Slide 53: Coaxial Cable
A good combination of high bandwidth and excellent interference immunity
  Higher bandwidth than twisted pair
  Cable TV distribution;
  Long distance telephone transmission
  Used in the original Ethernet LAN medium

## Slide 54: Optical Fiber
Light sources generate pulses of light that are transmitted on optical fiber
  Very long distances (>1000 km), and very high speeds (>40 Gbps/wavelength)
  Nearly error-free (Bit-Error-Rate of 10-15)
Profound influence on network architecture
  Dominates long distance transmission
  Distance less of a cost factor in communications
  Plentiful bandwidth for new services
Optical fiber
Optical
source
Modulator
Electrical
signal
Receiver
Electrical
signal

## Slide 55: Optical Fiber Properties
Advantages
Very low attenuation
Noise immunity
Extremely high bandwidth
Security: very difficult to tap without breaking
No corrosion
More compact & lighter than copper wire
Disadvantages
New types of optical signal impairments & dispersion
  Wavelength dependence
Limited bend radius
  If physical arc of cable too high, light lost or won’t reflect
  Will break
Difficult to splice
Mechanical vibration becomes signal noise
Notes: No corrosion: k bị ăn mòn

## Slide 56: Bit Rates of Digital Transmission Systems
System | Bit Rate (Bandwidth) | Observations
Telephone twisted pair | 33.6-56 kbps | 4 kHz telephone channel
Ethernet twisted pair | 10 Mbps, 100 Mbps | 100 meters of unshielded twisted copper wire pair
Cable modem | 500 kbps-4 Mbps | Shared CATV return channel
ADSL twisted pair | 64-640 kbps in, 1.536-6.144 Mbps out | Coexists with analog telephone signal
2.4 GHz radio | 2-11 Mbps | IEEE 802.11 wireless LAN
28 GHz radio | 1.5-45 Mbps | 5 km multipoint radio
Optical fiber | 2.5-10 Gbps | 1 wavelength
Optical fiber | >1600 Gbps | Many wavelengths

## Slide 57: Summary of the Lesson
  Different digital transmission systems have various bit rate, cost, bit-error-rate, and usages.