## Slide 1: Unit 02.01.01 CS 5220: COMPUTER COMMUNICATIONS
Peer-to-Peer Protocols and Services
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Peer-to-Peer Protocols
n – 1 peer process
n – 1 peer process
n peer process
n peer process
n + 1 peer process
n + 1 peer process
  
  
  
  

## Slide 3: Peer-to-Peer Protocols
Peer-to-Peer processes execute layer-n protocol to provide service to layer-(n+1)
Layer-(n+1) peer calls layer-n and passes Service Data Units (SDUs) for transfer
n – 1 peer process
n – 1 peer process
n peer process
n peer process
n + 1 peer process
n + 1 peer process
  
  
  
  
SDU

## Slide 4: Peer-to-Peer Protocols
Layer-n peers exchange Protocol Data Units (PDUs) to effect transfer
n – 1 peer process
n – 1 peer process
n peer process
n peer process
n + 1 peer process
n + 1 peer process
  
  
  
  
PDU

## Slide 5: Peer-to-Peer Protocols
Layer-n delivers SDUs to destination layer-(n+1) peer
n – 1 peer process
n – 1 peer process
n peer process
n peer process
n + 1 peer process
n + 1 peer process
  
  
  
  
SDU

## Slide 6: Service Models
The service model specifies the information transfer service layer-n provides to layer-(n+1)
The most important distinction is if the service is:
  Connection-oriented
  Connectionless
Quality-of-Service (QoS) requirement that specifies a level of performance that can be expected in the transfer of information.

## Slide 7: Examples of Services
Service model possible features:
  Arbitrary message size or structure
  Sequencing
  Reliability
  Timing
  Flow control
  Multiplexing
  Privacy, integrity, and authentication

## Slide 8: Message Size and Structure
What message size and structure will a service model accept?
  Different services impose restrictions on size & structure of data it will transfer Single bit? Block of bytes? Byte stream?
  Ex: Transfer of voice mail = 1 long message
  Ex: Transfer of voice call = byte stream
1 voice mail= 1 message = entire sequence of speech samples
(a)
1 call = sequence of 1-byte messages
(b)

## Slide 9: Segmentation & Blocking
1 long message
2 or more blocks
2 or more short messages
1 block
Segmentation & Reassembly: a layer breaks long messages into smaller blocks and reassembles these at the destination
Blocking & Unblocking: a layer combines small messages into bigger blocks prior to transfer

## Slide 10: Reliability & Sequencing
Reliability: what transmission is reliable?
  Sequencing: Are messages or information stream delivered in order? Or duplication?
How to provide reliable communication?
  Examples: TCP and HDLC
ARQ protocols combine error detection, retransmission, and sequence numbering to provide reliability

## Slide 11: Flow Control
Messages can be lost if receiving system does not have sufficient buffering to store arriving messages
If destination layer-(n+1) does not retrieve its information fast enough, destination layer-n buffers may overflow
Flow Control provide backpressure mechanisms that control transfer according to availability of buffers at the destination
Examples: TCP and HDLC

## Slide 12: Timing
Applications involving voice and video generate units of information that are related temporally
Destination application must reconstruct temporal relation in voice/video units
Network transfer introduces delay & jitter
Timing Recovery protocols use timestamps & sequence numbering to control the delay & jitter in delivered information
Examples: RTP & associated protocols in Voice over IP

## Slide 13: Multiplexing
Multiplexing enables multiple layer-(n+1) users to share a layer-n service
What it needs?
  A multiplexing tag is required to identify specific users at the destination
Examples: IP

## Slide 14: Privacy, Integrity, & Authentication
Privacy: ensuring that information transferred cannot be read by others
Integrity: ensuring that information is not altered during transfer
Authentication: verifying that sender and/or receiver are who they claim to be
Examples: IPSec, SSL

## Slide 15: End-to-End vs. Hop-by-Hop
A service feature can be provided by implementing a protocol
  end-to-end across the network
  across every hop in the network
Examples:
  Perform error control at every hop in the network or only between the source and destination?
  Perform flow control between every hop in the network or only between source & destination?

## Slide 16: Error control in Data Link Layer
1
2
Physical layer entity
Data link layer entity
3
Network layer entity
(a)
Data link
layer
Physical
layer
Physical
layer
Data link
layer
A
B
Packets
Packets
Frames
3
2
1
1
2
2
1
3
2
1
1
2
2
1
2
1
Medium
A
B
(b)
Data Link operates over wire-like, directly-connected systems
Frames can be corrupted or lost, but arrive in order
Data link performs error-checking & retransmission
Ensures error-free packet transfer between two systems

## Slide 17: Error Control in Transport Layer
Physical
layer
Data link
layer
Physical
layer
Data link
layer
End system
A
Network
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Transport
layer
Transport
layer
Messages
Messages
Segments
End system
B
Network

## Slide 18: Which Approach Preferred
More scalable if complexity at the edge
Simple inside the network
1
2
5
Data
ACK/NAK
End-to-end (TCP)
3
Data
4
Data
Data
Hop-by-hop cannot ensure E2E correctness
1
2
5
Data
ACK/NAK
Hop-by-hop (HDLC)
3
Data
ACK/NAK
4
Data
ACK/NAK
Data
ACK/NAK
Faster recovery

## Slide 19: Summary of the Lesson
There is a basic tradeoff in choosing end-to-end and hop-by-hop approaches.

## Slide 20: Unit 02.01.01 CS 5220: COMPUTER COMMUNICATIONS
Stop-and-Wait ARQ Protocol
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 21: Automatic Repeat Request (ARQ)
Purpose: to ensure a sequence of information packets is delivered in order and without errors or duplications despite transmission errors & losses
Sliding window: a set of Seq.# corresponding to frames permitted to send or receive.

## Slide 22: Automatic Repeat Request (ARQ) - CONT
Three ARQ protocols
  Stop-and-Wait ARQ
  Go-Back N ARQ
  Selective Repeat ARQ
Basic elements of ARQ:
  Error-detecting code with high error coverage
  ACKs (positive acknowledgments)
  NAKs (negative acknowledgments)
  Timeout mechanism

## Slide 23: Stop-and-Wait ARQ
CRC
Information
packet
Header
Information frame
Control frame: ACKs
CRC
Header
Packet
Error-free
packet
Information frame
Control frame
Transmitter
(Process A)
Receiver
(Process B)
Timer set after each frame transmission
Transmit a frame, wait for ACK

## Slide 24: Need for Sequence Numbers
  In cases (a) & (b) the transmitting station A acts the same way
  But in case (b) the receiving station B accepts frame 1 twice
(a) Frame 1 lost
A
B
Frame 0
Frame 1
ACK
Frame 1
ACK
Time
Time-out
Frame 2
(b) ACK lost
A
B
Frame 0
Frame 1
ACK
Frame 1
ACK
Time
Time-out
Frame 2
ACK

## Slide 25: Sequence Numbers in ACK
  The transmitting station A misinterprets duplicate ACKs
  Incorrectly assumes second ACK acknowledges Frame 1
(c) Premature Time-out
A
B
Frame 0
Frame 0
ACK
Frame 1
ACK
Time
Time-out
Frame 2

## Slide 26: 1-Bit Sequence Numbering Suffices
(0,0)
(0,1)
(1,0)
(1,1)
Global State:
(Slast, Rnext)
Error-free frame 0
arrives at receiver
ACK for
frame 0
arrives at
transmitter
ACK for
frame 1
arrives at
transmitter
Error-free frame 1
arrives at receiver
Transmitter A
Receiver B
Slast
Rnext
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
Timer
Rnext
Slast

## Slide 27: Stop-and-Wait ARQ
Transmitter
Ready state
Await request from higher layer for packet transfer
When request arrives, transmit frame with updated Slast and CRC
Go to Wait State
Wait state
Wait for ACK or timer to expire; block requests from higher layer
If timeout expires
  retransmit frame and reset timer
If ACK received:
  If sequence number is incorrect or if errors detected: ignore ACK
  If sequence number is correct (Rnext = Slast +1): accept frame, go to Ready state
Receiver
Always in Ready State
Wait for arrival of new frame
When frame arrives, check for errors
If no errors detected and sequence number is correct (Slast=Rnext), then
  accept frame,
  update Rnext,
  send ACK frame with Rnext,
  deliver packet to higher layer
If no errors detected and wrong sequence number
  discard frame
  send ACK frame with Rnext
If errors detected
  discard frame

## Slide 28: Summary: Applications of Stop-and-Wait ARQ
IBM Binary Synchronous Communications protocol (Bisync): character-oriented data link control
Xmodem: modem file transfer protocol
Trivial File Transfer Protocol (RFC 1350): simple protocol for file transfer over UDP

## Slide 29: Unit 02.01.03 CS 5220: COMPUTER COMMUNICATIONS
S&W Performance, and Go-back-N ARQ
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 30: Stop-and-Wait Performance
Stop-and-Wait ARQ works well on channels that have low propagation delay
The protocol becomes inefficient when the propagation delay is much greater than the time to transmit a frame

## Slide 31: Stop-and-Wait ARQ Efficiency
A
B
First frame bit enters channel
Last frame bit enters channel
Channel idle while transmitter waits for ACK
Last frame bit arrives at receiver
Receiver processes frame and
prepares ACK
ACK arrives
First frame bit arrives at receiver
t
t

## Slide 32: Stop-and-Wait Delay Model
frame
tf time (nf/R)
A
B
tprop
tack (na/R)
tproc
tprop
tproc
      t0 = total time to transmit 1 frame
bits/info frame
channel transmission rate
bits/ACK frame
ACK

## Slide 33: S&W Efficiency on Error-free channel
bits for header & CRC
Effect of
frame overhead
Effect of
ACK frame
Effect of
Delay-Bandwidth Product
Effective transmission rate:
Transmission efficiency:

## Slide 34: Delay-Bandwidth Product
frame
tf time (nf/R)
A
B
tprop
tack (na/R)
tproc
tprop
tproc
      t0 = total time to transmit 1 frame
Delay-bandwidth product is 2( tprop + tproc ) * R, or RTT * R

## Slide 35: Example: Impact of Delay-Bandwidth Product
nf=1250 bytes = 10000 bits, na=no=25 bytes = 200 bits
2xDelayxBW Efficiency | 1 ms 200 km (RTT dist.) | 10 ms 2000 km | 100 ms 20000 km | 1 sec 200000 km
1 Mbps | 103 88% | 104 49% | 105 9% | 106 1%
1 Gbps | 106 1% | 107 0.1% | 108 0.01% | 109 0.001%

## Slide 36: S&W Efficiency in Channel with Errors
Let 1 – Pf = probability frame arrives w/o errors
Avg. # of transmissions to first correct arrival is then 1/ (1–Pf )
“If 1-in-10 get through without error, then avg. 10 tries to success”
Avg. Total Time per frame is then t0/(1 – Pf)
Effect of frame loss

## Slide 37: Example: Impact Bit Error Rate
nf=1250 bytes = 10000 bits, na=no=25 bytes = 200 bits
Find efficiency for random bit errors with p=0, 10-6, 10-5, 10-4
1 – Pf Efficiency | 0 | 10-6 | 10-5 | 10-4
1 Mbps & 1 ms | 1 88% | 0.99 86.6% | 0.905 79.2% | 0.368 32.2%

## Slide 38: Go-Back-N ARQ
Improve Stop-and-Wait by not waiting!
Keep channel busy by continuing to send frames
A procedure where the transmission of a new frame is begun before the completion time of the previous frame transmission is said to be pipelining.

## Slide 39: Go-Back-N
Allow a window of up to Ws outstanding frames
  Receiver’s window size is often 1
The window size must be larger than the delay-bandwidth product to ensure that the channel is kept full
If ACK for oldest frame arrives before window is exhausted, continue transmitting
If window is exhausted, pull back and retransmit all outstanding frames

## Slide 40: Go-Back-4
  Frame with errors and subsequent out-of-sequence frames are ignored
  Transmitter is forced to go back when window of 4 is exhausted
A
B
fr
0
Time
fr
1
fr
2
fr
3
fr
4
fr
5
fr
6
fr
3
ACK1
out of sequence frames
Go-Back-4:
4 frames are outstanding; so go back 4
fr
5
fr
6
fr
4
fr
7
fr
8
fr
9
ACK2
ACK3
ACK4
ACK5
ACK6
ACK7
ACK8
ACK9
Rnext 0 1 2 3 3 4 5 6 7 8 9

## Slide 41: Summary of the Lesson
Delay-bandwidth product is a key element in performance evaluation of network protocols
Stop-and-wait is only efficient if the delay-bandwidth product is very small

## Slide 42: Unit 02.01.04 CS 5220: COMPUTER COMMUNICATIONS
Go-back-N and Selective Repeat ARQ
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 43: Go-Back-N with Timeout
Problem with Go-Back-N as presented:
  Window size should be long enough to cover round trip time
  If a frame is lost and transmitter does not have a frame to send, then window will not be exhausted and recovery will not commence

## Slide 44: Go-Back-N with Timeout
Use a timeout with each frame
  When timeout expires, resend all outstanding frames
A
B
Time
fr
0
fr
0
Time-out expires
fr
1
ACK1
Receiver is looking for Rnext = 0

## Slide 45: Maximum Window Size
Given m-bit seq. numbers, what is the maximum number of frames that can be outstanding in “go back N”?
MAX_SEQ = 2^m – 1 while there are 2^m sequence numbers. Should the maximum number be MAX_SEQ or MAX_SEQ + 1?
Example: m = 2; sequence numbers: 0, 1, 2, 3
1) Sender sends 4 frames in a row, from 0 through 3
2) Receiver sends four corresponding ACKs back to sender, but all lost!
3) Sender times out, re-sends the 4 frames (0 through 3)
4) Receiver is waiting for frame 0
Can receiver determine whether this is a new frame 0 or an old frame 0?

## Slide 46
A
B
fr
0
Time
fr
1
fr
2
fr
3
fr
0
fr
1
fr
2
fr
3
ACK1
M = 22 = 4, Go-Back - 4:
ACK
0
ACK2
ACK3
Transmitter goes back 4
Receiver has Rnext= 0, but it does not know whether its ACK for frame 0 was received, so it does not know whether this is the old frame 0 or a new frame 0
Maximum Allowable Window Size is Ws = 2m
Rnext 0 1 2 3 0

## Slide 47
Maximum Allowable Window Size is Ws = 2m-1
A
B
fr
0
Time
fr
1
fr
2
fr
0
fr
1
fr
2
ACK1
M = 22 = 4, Go-Back-3:
ACK2
ACK3
Transmitter goes back 3
Receiver has Rnext= 3 , so it rejects the old frame 0
Rnext 0 1 2 3
The sequence of frame exchange.

## Slide 48: Applications of Go-Back-N ARQ
HDLC (High-Level Data Link Control): bit-oriented data link control
V.42 modem: error control over telephone modem links

## Slide 49: Piggybacking and Bidirectional Links
Since in the two-way transmission, data frames and ACK frames are interleaving, why not have a “free” ride of ACK upon a data delivering?
  Piggybacking: receiver inserts ACK in the next departing frame
  For piggybacking, how long should the data link layer wait for a packet onto which to piggyback the ACK?
Transmitter A
Receiver B
Slast
Rnext

## Slide 50: Required Timeout & Window Size
Tf
Tf
Tproc
Tprop
Tprop
Tout
Timeout value should allow for:
  Two propagation times + two transmission times + 1 processing time: 2 Tprop + 2 Tf + Tproc; Assume receiver starts transmission right after receiving
Ws should be large enough to keep channel busy for Tout

## Slide 51: Window Size for Delay-Bandwidth Product
Frame = 1250 bytes =10,000 bits, R = 1 Mbps |  | 
Delay: 2(tprop + tproc) | Delay x BW | Window (1 + D * W / L)
1 ms | 1000 bits | 1
10 ms | 10,000 bits | 2
100 ms | 100,000 bits | 11
1 second | 1,000,000 bits | 101

## Slide 52: Selective Repeat ARQ
Why Go-Back-N ARQ inefficient?
  because multiple frames are resent when errors or losses occur
  Correct but out-of-sequence frames would be discarded (because receiver buffer only 1)

## Slide 53: Selective Repeat ARQ
Selective Repeat retransmits only an individual frame
  Timeout causes individual corresponding frame to be resent
  NAK causes retransmission of oldest un-acked frame
Receiver maintains a receive window of sequence numbers that can be accepted
  Receiver window is increased larger
  Error-free, but out-of-sequence frames with sequence numbers within the receive window are buffered
  Arrival of frame with Rnext causes window to slide forward by 1 or more

## Slide 54: Selective Repeat ARQ
A
B
fr
0
Time
fr
1
fr
2
fr
3
fr
4
fr
5
fr
6
fr
2
ACK1
fr
8
fr
9
fr
7
fr
10
fr
11
fr
12
ACK2
NAK2
ACK7
ACK8
ACK9
ACK10
ACK11
ACK12
ACK2
ACK2
ACK2

## Slide 55: What size Ws and Wr allowed?
Example (as in Go-back N): M=22=4, Ws=3, Wr=3
A
B
fr0
Time
fr1
fr2
fr0
ACK1
ACK2
ACK3
Frame 0 resent
{0,1,2}
{1,2}
{2}
{.}
Send Window
{0,1,2}
{1,2,3}
Receive Window
{2,3,0}
{3,0,1}
Old frame 0 accepted as a
new frame because it falls
in the receive window

## Slide 56: Ws + Wr = 2m is maximum allowed
Example: M=22=4, Ws=2, Wr=2
A
B
fr0
Time
fr1
fr0
ACK1
ACK2
Frame 0 resent
{0,1}
{1}
{.}
Send Window
{0,1}
{1,2}
Receive Window
{2,3}
Old frame 0 rejected because it falls outside the receive window

## Slide 57: Applications of Sel. Repeat ARQ
TCP (Transmission Control Protocol): transport layer protocol uses variation of selective repeat to provide reliable stream service
Service Specific Connection Oriented Protocol: error control for signaling messages in ATM networks

## Slide 58: Efficiency of Selective Repeat
Assume Pf frame loss probability, then number of transmissions required to deliver a frame is 1/(1-Pf):
  Average transmission time: tf /(1-Pf)
frame
tf time (nf/R)
A
B
tprop
Tack (na/R)
tproc
tprop
tproc
      t0 = total time to transmit 1 frame

## Slide 59: Comparison of ARQ Efficiencies
Selective-Repeat:
Go-Back-N:
Stop-and-Wait:
Assume na, no are negligible relative to nf, and L = 2(tprop+tproc)R/nf , Ws= L+1
For Pf≈0, SR & GBN same
For Pf→1, GBN & SW same

## Slide 60: Summary: Impact Bit Error Rate on ARQ
nf=1250 bytes = 10000 bits, na=no=25 bytes = 200 bits
Compare S&W, GBN & SR efficiency for random bit errors with p=0, 10-6, 10-5, 10-4 and R = 1 Mbps & 100 ms
Efficiency | 0 | 10-6 | 10-5 | 10-4
S&W | 8.9% | 8.8% | 8.0% | 3.3%
GBN | 98% | 88.2% | 45.4% | 4.9%
SR | 98% | 97% | 89% | 36%