## Slide 1: Unit 02.02.01 CS 5220: COMPUTER COMMUNICATIONS
TCP Reliable Stream and Flow Control
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: TCP ARQ Model
TCP reliable stream service
  Connection-oriented
  Error free, without duplication, in order of sequence
TCP uses Selective Repeat ARQ
  Transfers byte stream without preserving boundaries

## Slide 3: TCP Reliable Stream Service
Send buffer
Segments
Receive buffer
Application Layer writes bytes into send buffer through socket
ACKs
Transmitter
Receiver
Application Layer reads bytes from receive buffer through socket
TCP transfers byte stream in order, without errors or duplications
Application layer
Transport layer
Write 45 bytes
Write 15 bytes
Write 20 bytes
Read 40 bytes
Read 40 bytes

## Slide 4: TCP ARQ Environment
Operates over best effort service of IP that is not wirelike
  Packets can arrive with errors or be lost
  Packets can arrive out-of-order
  Packets can arrive after very long delays
  Old segments from previous connections may arrive, so detection and elimination of duplicates is hard

## Slide 5: TCP ARQ Sequence #
Sequence Numbers
  Seq. # is number of first byte in segment payload
  Very long Seq. #s (32 bits) to deal with long delays
  Initial sequence numbers negotiated during connection setup (to deal with very old duplicates)
  Accept segments within a receive window
  Timeout at the end of connection to clear old segments

## Slide 6: TCP Connections
TCP Connection
  Identified uniquely by Send IP Address, Send TCP Port #, Receive IP Address, Receive TCP Port #
Connection Setup with Three-Way Handshake
  Three-way exchange to negotiate initial Seq. #’s for connections in each direction
Data Transfer
  Exchange segments carrying data
Graceful Close
  Close each direction separately

## Slide 7: 1st Handshake
SYN bit set indicates request to establish connection from client to server
Initial Seq. # from client to server

## Slide 8
Transmitter
Slast
Slast + Ws – 1
...
Send Window
Srecent
bytes
transmitted
& ACKed
...
...
Slast + Wa-1
Slast oldest unacknowledged byte
Srecent highest-numbered transmitted byte
Slast+Wa-1 highest-numbered byte that can be transmitted
Slast+Ws-1 highest-numbered byte that can be accepted from the application
Receiver
Receive Window
Rnext
Rlast
Rlast + WR – 1
Rlast highest-numbered byte not yet read by the application
Rnext next expected byte
Rnew highest numbered byte received correctly
Rlast+WR-1 highest-numbered byte that can be accommodated in receive buffer
Rnew

## Slide 9: TCP Data Exchange
Application Layers write bytes into buffers
TCP sender forms segments
  When bytes exceed threshold or timer expires
  Upon PUSH command from applications
  Consecutive bytes from buffer inserted in payload
  Sequence # & ACK # inserted in header
  Checksum calculated and included in header
TCP receiver
  Performs selective repeat ARQ functions
  Writes error-free, in-sequence bytes to receive buffer

## Slide 10: TCP Sequence #
The segment contains a sequence number that corresponds to the number of the first byte in the string that is being transmitted
  Significantly differs from ARQs

## Slide 11: TCP Flow Control
TCP receiver controls rate at which sender transmits to prevent buffer overflow
TCP receiver advertises a window size specifying number of bytes that can be accommodated by receiver
WA = WR – (Rnew – Rlast)
TCP sender obliged to keep # outstanding bytes below WA
(Srecent - Slast) ≤ WA
Receive Window
Rlast
Rlast + WR – 1
Rnew
WA
Slast
Slast + Ws – 1
...
Send Window
Srecent
...
...
Slast + WA-1

## Slide 12: TCP Retransmission Timeout
TCP retransmits a segment after timeout period
  Timeout too short: excessive number of retransmissions
  Timeout too long: recovery too slow
  Timeout depends on RTT: time from when segment is sent to when ACK is received
Round trip time (RTT) in Internet is highly variable
  Routes vary and can change in mid-connection
  Traffic fluctuates

## Slide 13: Adaptive RTT
TCP uses adaptive estimation of RTT
  Measure RTT each time ACK received: tn
  tRTT(new) = a tRTT(old) + (1 – a) tn
  a = 7/8 typical

## Slide 14: RTT Variability
Estimate variance s2 of RTT variation
Estimate for timeout:
  tout = tRTT + k sRTT
If RTT highly variable, timeout increase accordingly
If RTT nearly constant, timeout close to RTT estimate
In practice, approximate estimation of deviation
    dRTT(new) = b dRTT(old) + (1-b) | tn - tRTT |
tout = tRTT + 4 dRTT

## Slide 15: Summary of the Lesson
TCP flow control is based on selective repeat ARQ, yet varies in several key aspects.

## Slide 16: Unit 02.02.02 CS 5220: COMPUTER COMMUNICATIONS
Framing and PPP
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 17: Data Link Protocols
Directly connected, wire-like
Losses & errors, but no out-of-sequence frames
Applications: Direct Links; LANs; Connections across WANs
Data Links Services
Framing
Error control
Flow control
Multiplexing
Link Maintenance
Security: Authentication & Encryption
Examples
PPP
HDLC
Ethernet LAN
IEEE 802.11 (Wi Fi) LAN
Data link
layer
Physical
layer
Physical
layer
Data link
layer
A
B
Packets
Packets
Frames

## Slide 18: Framing
Mapping stream of physical layer bits into frames
Mapping frames into bit stream
Frame boundaries can be determined using:
  Character Counts
  Control Characters
  Flags
  CRC Checks
0110110111
Framing
received
frames
0111110101
transmitted
frames

## Slide 19: Character-Oriented Framing (Byte Stuffing)
Data to be sent
A
DLE
B
ETX
DLE
STX
E
After stuffing and framing
DLE
DLE
B
ETX
DLE
DLE
STX
DLE
STX
A
E
DLE
ETX
Frames consist of integer number of bytes
Special 8-bit patterns used as control characters
Byte used to carry non-printable characters in frame
  DLE (data link escape) = 0x10
  DLE STX (DLE ETX) used to indicate beginning (end) of frame
  Insert extra DLE in front of occurrence of DLE STX (DLE ETX) in frame
  All DLEs occur in pairs except at frame boundaries

## Slide 20: Flag-based Framing & Bit Stuffing
Flag-based frame synchronization is for transferring an arbitrary number of bits within a frame
Flag
Flag
Address
Control
Information
FCS
HDLC frame
any number of bits

## Slide 21: Bit Stuffing
Frame delineated by flag character
It uses bit stuffing to prevent occurrence of flag 01111110 (HEX 7E) inside the frame
Transmitter inserts extra 0 after each consecutive five 1s inside the frame
Receiver checks for five consecutive 1s
  if next bit = 0, it is removed
  if next two bits are 10, then flag is detected
  If next two bits are 11, then frame has errors

## Slide 22: Example: Bit stuffing & de-stuffing
0110111111111100
Data to be sent
After stuffing and framing
0111111001101111101111100001111110
(a)
0110111111111100
Data received
After destuffing and deframing
(b)
0111111001101111101111100001111110

## Slide 23: PPP: Point-to-Point Protocol
Data link protocol for point-to-point lines in Internet
  Router-router; dial-up to router
1. Provides Framing and Error Detection
  Character-oriented HDLC-like frame structure
2. Link Control Protocol
  Bringing up, testing, bringing down lines; negotiating options
  Authentication: key capability in ISP access
3. A family of Network Control Protocols specific to different network layer protocols
  IP, OSI network layer, IPX (Novell), Appletalk

## Slide 24: PPP Frame
PPP uses similar frame structure as HDLC, except
  Protocol type field
  Payload contains an integer number of bytes
PPP uses the same flag, but uses byte stuffing
Problems with PPP byte stuffing
  Size of frame varies unpredictably due to byte insertion
  Malicious users can inflate bandwidth by inserting 7D & 7E
Flag
Flag
Address
Control
Information
CRC
Protocol
01111110
01111110
1111111
00000011
Unnumbered frame
Specifies what kind of packet is contained in the payload, e.g., LCP, NCP, IP, OSI CLNP, IPX
All stations are to
accept the frame
integer # of bytes

## Slide 25: Byte-Stuffing in PPP
PPP is character-oriented version of HDLC
Flag is 0x7E (01111110)
Control escape 0x7D (01111101)
Any occurrence of flag or control escape inside of frame is replaced with 0x7D followed by original octet XORed with 0x20 (00100000)
Data to be sent
41
7D
42
7E
50
70
46
After stuffing and framing
5D
42
7D
5E
50
70
46
7E
41
7D
7E

## Slide 26: PPP Applications
PPP used in many point-to-point applications
Telephone Modem Links 30 kbps
Packet over SONET 600 Mbps to 10 Gbps
  IP→PPP→SONET
PPP is also used over shared links such as Ethernet to provide LCP, NCP, and authentication features
  PPP over Ethernet (RFC 2516)
  Used over DSL

## Slide 27: PPP Authentication
Password Authentication Protocol
  Initiator must send ID & password
  Authenticator replies with authentication success/fail
  After several attempts, LCP closes link
  Transmitted unencrypted, susceptible to eavesdropping
Challenge-Handshake Authentication Protocol (CHAP)
  Initiator & authenticator share a secret key
  Authenticator sends a challenge (random # & ID)
  Initiator computes cryptographic checksum of random # & ID using the shared secret key
  Authenticator calculates cryptocgraphic checksum & compares to response
  Authenticator can reissue challenge during session
Notes: LCP = link control protocol

## Slide 28: Summary
Bit stuffing and byte stuffing are used for framing
PPP uses byte stuffing
CHAP is a security protocol

## Slide 29: Unit 02.02.03 CS 5220: COMPUTER COMMUNICATIONS
HDLC, Multiplexing
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 30: High-Level Data Link Control (HDLC)
Bit-oriented data link control
Derived from IBM Synchronous Data Link Control (SDLC)
Related to Link Access Procedure Balanced (LAPB)
  LAPD in ISDN
  LAPM in cellular telephone signaling

## Slide 31
Physical
layer
Data link
layer
Data link
layer
Network
layer
DLSDU
DLSDU
Network
layer
Physical
layer
DLPDU
NLPDU
“Packet”
“Frame”
DLSAP
DLSAP

## Slide 32: HDLC Data Transfer Modes
Normal Response Mode (NRM)
  Used in polling multi-drop lines
Asynchronous Balanced Mode (ABM)
  Used in full-duplex point-to-point links
Primary
Commands
Responses
Secondary
Secondary
Secondary
Primary
Secondary
Commands
Responses
Primary
Secondary
Commands
Responses

## Slide 33: HDLC Frame Format
Control field gives HDLC its functionality
Codes in fields have specific meanings and uses
  Flag: delineate frame boundaries
  Address: identify secondary station (1 or more octets)
    In ABM mode, a station can act as primary or secondary so address changes accordingly
  Control: purpose & functions of frame (1 or 2 octets)
  Information: contains user data; length not standardized, but implementations impose maximum
  Frame Check Sequence: 16- or 32-bit CRC
Flag
Flag
Address
Control
Information
FCS

## Slide 34: Control Field Format
0
N(S)
N(R)
P/F
1
2-4
5
6-8
Information Frame
N(R)
P/F
Supervisory Frame
1
0
S
S
Unnumbered Frame
P/F
1
1
M
M
M
M
M

## Slide 35: Error Detection & Loss Recovery
Frames lost due to loss-of-synch or receiver buffer overflow
Frames may undergo errors in transmission
CRCs detect errors and such frames treated as lost
Recovery through ACKs, timeouts & retransmission
Sequence numbering to identify out-of-sequence & duplicate frames
HDLC provides for options that implement several ARQ methods

## Slide 36: Statistical Multiplexing
Buffer
A
B
C
Input lines
Output line
Header Data payload
Multiplexing concentrates bursty traffic onto a shared line
Greater efficiency and lower cost

## Slide 37: Tradeoff Delay for Efficiency
A1
A2
B1
B2
C2
C1
A2
B1
B2
C2
C1
(a)
(b)
A1
Shared lines
Dedicated lines
Dedicated lines involve not waiting for other users, but lines are used inefficiently when user traffic is bursty
Shared lines concentrate packets into shared line; packets buffered (delayed) when line is not immediately available

## Slide 38: Multiplexers inherent in Packet Switches
1
2
N
1
2
N






Packets/frames forwarded to buffer (queue) prior to transmission from switch
Multiplexing occurs in these buffers; FIFIO vs priority scheduling

## Slide 39: Delay and Utilization Tradeoff
Buffering introduces packet delay
Buffer overflow introduces packet loss
End-to-end protocols deals with loss

## Slide 40: Multiplexer Modeling
Buffer
Output line
Input lines
A
B
C
Arrivals: What is the packet inter-arrival pattern?
Service Time: How long are the packets?
Service Discipline: What is order of transmission?
Buffer Discipline: If buffer is full, which packet is dropped?
Performance Measures: Delay Distribution; Packet Loss Probability; Line Utilization

## Slide 41: Delay = Waiting + Service Times
Packet arrives
at queue
Packet begins
transmission
Packet completes
transmission
Service
time
Waiting
time
P1
P1
P2
P2
P3
P3
P4
P4
P5
P5

## Slide 42: Delay = Waiting + Service Times
Packets arrive and wait for service
Waiting Time: from arrival instant to beginning of service
Service Time: time to transmit packet
Delay: total time in system = waiting time + service time

## Slide 43: Fluctuations in Packets in the System
A1
A2
B1
B2
C2
C1
A2
B1
B2
C2
C1
(a)
(b)
A1
Shared line
Dedicated lines
(c)
N(t)
Number of packets in the system

## Slide 44: Poisson Arrivals & Queuing
Average Arrival Rate: l packets per second
Arrivals are equally-likely to occur at any point in time
Time between consecutive arrivals is an exponential random variable with mean 1/ l
Number of arrivals in interval of time t is a Poisson random variable with mean lt

## Slide 45: Summary
Multiplexing makes good tradeoff of delay and utilization
Queueing involves sophisticated modeling and analysis