## Slide 1: Unit 02.03.01 CS 5220: COMPUTER COMMUNICATIONS
Medium Access Control
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Medium Access Control
Broadcast LANs
  Simple and Cheap
  All information sent to all users
  No routing
Medium Access Control
  How to coordinate access to shared medium

## Slide 3: Multiple Access Communications
Shared media basis for broadcast networks
  Inexpensive: radio over air; copper or coaxial cable
  M users communicate by broadcasting into medium
Key issue: How to share the medium when there is a competition for it?

1
2
3
4
5
M
Shared multiple
access medium

## Slide 4: Approaches to Media Sharing
Medium sharing techniques
Static channelization
Dynamic medium access control
Scheduling
Random access
Partition medium
Dedicated allocation to users
Satellite transmission
Cellular Telephone
Polling: take turns
Request for slot in transmission schedule
Token ring
Wireless LANs
Loose coordination
Send, wait, retry if necessary
Aloha
Ethernet

## Slide 5: Channelization Example: Satellite
Satellite Channel
uplink fin
downlink fout

## Slide 6: Channelization: Cellular
uplink f1 ; downlink f2
uplink f3 ; downlink f4

## Slide 7: Why Channelization?
Channelization
  Semi-static bandwidth allocation of portion of shared medium to a given user
Highly efficient for constant-bit rate traffic
Preferred approach in
  Cellular telephone networks
  Terrestrial & satellite broadcast radio & TV

## Slide 8: Channelization Approaches
Frequency Division Multiple Access (FDMA)
  Frequency band allocated to users
  Broadcast radio & TV, analog cellular phone
Time Division Multiple Access (TDMA)
  Periodic time slots allocated to users
  Telephone backbone, GSM digital cellular phone
Code Division Multiple Access (CDMA)
  Code allocated to users
  Cellular phones, 3G cellular

## Slide 9: Why not Channelization?
Inflexible in allocation of bandwidth to users with different requirements
Inefficient for bursty traffic
Does not scale well to large numbers of users
Dynamic MAC much better at handling bursty traffic

## Slide 10: Scheduling: Token-Passing
Ring networks
token
Station that holds token transmits into ring
Data to M

## Slide 11: Scheduling: Polling
Inbound line
Outbound line
Host
computer
Stations
1
2
3
M
Poll 1
Data from 1

## Slide 12: Random Access
Multi-tapped (mulit-access) Bus
Transmit when ready
Collision!!
Transmission collisions can occur; need retransmission strategy

## Slide 13: Delay-Bandwidth Product
Delay-bandwidth product is key parameter
  Coordination in sharing medium involves using bandwidth (explicitly or implicitly)
  Difficulty of coordination commensurate with delay-bandwidth product
Delay-bandwidth product is 2( tprop + tproc ) * R, or RTT * R (if tproc is negligible)

## Slide 14: Two-Station Example
Simple two-station example
  Station with frame to send listens to channel and transmits if channel found idle
  Station monitors channel to detect collision
  If collision occurs, station that begin transmitting earlier retransmits (the propagation time is fixed & known between two stations)
A
B

## Slide 15: Two-Station MAC Example – CASE I
Two stations are trying to share a common channel
A transmits at t = 0
Distance d meters
tprop = d /  seconds
A
B
A
B
B does not transmit before t = tprop & A captures channel
Case 1

## Slide 16: Two-Station MAC Example – Case II
Two stations are trying to share a common medium
A transmits at t = 0
Distance d meters
tprop = d /  seconds
A
B
B transmits before t = tprop and detects collision soon
thereafter
A
B
A
B
A detects
collision at
t = 2 tprop
Case 2

## Slide 17: Efficiency of Two-Station Example
Each frame transmission requires 2tprop of quiet time
  Station B needs to be quiet tprop before and after time when Station A transmits
  R transmission bit rate (bandwidth)
  L bits/frame

## Slide 18: Summary: Normalized Delay-Bandwidth
Propagation delay
Time to transmit a frame
Normalized Delay-bandwidth product plays a key role in performance of medium access control protocols

## Slide 19: Unit 02.03.02 CS 5220: COMPUTER COMMUNICATIONS
MAC Random Access - ALOHA
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 20: Random Access
Random access
  No scheduling overhead
  Delay-bandwidth product is important factor
  Uniform frame size

## Slide 21: ALOHA
Wireless link to provide data transfer between campuses of University of Hawaii, a simple scheme
  A station transmits whenever it has data to transmit
  If more than one frames are transmitted, they collide with each other and lost
  If ACK not received within timeout, then a station picks random backoff
  Station retransmits frame after backoff time
t
t0
t0-X
t0+X
t0+X+2tprop
t0+X+2tprop + B
Vulnerable
period
Time-out
Backoff period B
First transmission
Retransmission

## Slide 22: ALOHA Model
Definitions and assumptions
  X: frame transmission time (assume constant)
  S: throughput (average # successful frame transmissions per X seconds)
  G: load (average # transmission attempts per X sec.)
  Psuccess : probability a frame transmission is successful
X
X
Reference frame transmission
Prior interval
Any transmission that begins during vulnerable period leads to collision
Success if no arrivals during 2X seconds

## Slide 23: Abramson’s Assumption
What is probability of no arrivals in vulnerable period?
  Abramson assumption: Effect of backoff algorithm is that frame arrivals are equally likely to occur at any time interval
  G is avg. # arrivals per X seconds, divide X into n intervals of duration D = X/n
  p = probability of arrival in D interval, then G = n p since n intervals in X seconds
S = Ge-2G

## Slide 24: Slotted ALOHA
ALOHA performance depends on probability of collisions
Reducing vulnerable period can reduce collision probability
Slotted ALOHA reduces collision probability by constraining the stations to transmit in synchronized manner.

## Slide 25: Slotted ALOHA Model
Time is slotted in X seconds slots (X is frame transmission time)
Stations synchronized to frame times (may incur waiting time)
Stations transmit frames only at the beginning of a time slot
Backoff intervals in multiples of slots
t
(k+1)X
kX
t0 +X+2tprop+ B
Vulnerableperiod
Time-out
Backoff period B
t0 +X+2tprop

## Slide 26: Throughput of Slotted ALOHA
Ge-G
Ge-2G
G
S
1/2e = 0.184
1/e=0.368

## Slide 27: Summary
ALOHA schemes are simple, but low maximum system throughput

## Slide 28: Unit 02.03.03 CS 5220: COMPUTER COMMUNICATIONS
Random Access: CSMA & CSMA-CD
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 29: CSMA
Carrier Sensing Multiple Access (CSMA)
  When collisions occur they involve entire frame transmission time
  Sensing for detecting an ongoing transmission
  Avoids transmission certain to cause collisions

## Slide 30: Carrier Sensing Multiple Access (CSMA)
A
Station A begins transmission at t = 0
A
Station A captures
channel at t = tprop
A station senses the channel before it starts transmission
  If busy, either wait or schedule backoff (different options)
  If idle, start transmission
  Vulnerable period is reduced to tprop (due to channel capture effect)

## Slide 31: CSMA Options: 1-persistent CSMA
Transmitter behavior when busy channel is sensed
  1-persistent CSMA (most greedy)
    Start transmission as soon as the channel becomes idle
    Low delay and low efficiency

## Slide 32: 1-Persistent CSMA Throughput
0.53
0.45
0.16
S
G
a = 0.01
a =0.1
a = 1
Normalized propagation delay a (tprog/X)
Better than Aloha & slotted Aloha for small a
Worse than Aloha for a > 1

## Slide 33: CSMA Options
  Non-persistent CSMA (least greedy)
    If busy, wait a backoff period, then sense carrier again
    High delay and high efficiency
  p-persistent CSMA (adjustable greedy)
    Wait till channel becomes idle, transmit with probability p; or wait one tprop & re-sense with probability 1-p
    Delay and efficiency can be balanced
Sensing

## Slide 34: Non-Persistent CSMA Throughput
0.81
0.51
0.14
S
G
a = 0.01
a = 0.1
a = 1
Higher maximum throughput than 1-persistent for small a
Worse than Aloha for a > 1

## Slide 35: CSMA with Collision Detection (CSMA/CD)
Monitor for collisions & abort transmission
  Stations with frames to send, first do carrier sensing
  After beginning transmissions, stations continue listening to the medium to detect collisions
  If collisions detected, all stations involved abort transmission, reschedule random backoff times, and try again at scheduled times - quickly terminating a damaged frame saves time & bandwidth (T_trans >> T_prog)
  In CSMA, collisions result in wastage of entire frame transmission time
  CSMA-CD reduces wastage to time to detect collision & abort transmission

## Slide 36: CSMA/CD reaction time
It takes 2 tprop to find out if channel has been captured
A begins to
transmit at
t = 0
A
B
B begins to
transmit at
t = tprop- ;
B detects
collision at
t = tprop
A
B
A
B
A detects
collision at
t= 2 tprop- 

## Slide 37: CSMA-CD Model
  Collisions can be detected and resolved in 2tprop
  Time slotted in 2tprop slots during contention periods
  Once the contention period is over (a station successfully occupies the channel), it takes X seconds for a frame to be transmitted
  It takes tprop before the next contention period starts.
Busy
Contention
Busy
Time
Idle
Contention
Busy

## Slide 38: Contention Resolution
Contention is resolved if exactly 1 station transmits in a slot
  Assume n busy stations, and each may transmit with probability p in each contention time slot
  By taking derivative of Psuccess we find max occurs at p=1/n
  On average, 1/Pmax = e = 2.718 time slots to resolve contention

## Slide 39: CSMA/CD Throughput
At maximum throughput, systems alternates between contention periods and frame transmission times
where:
  R bits/sec, L bits/frame, X=L/R seconds/frame
  a = tprop/X (normalized propagation delay)
  n meters/sec.
  d meters is diameter of system
  2e+1 = 6.44

## Slide 40: Summary: Throughput for Random Access MACs
ALOHA
Slotted ALOHA
1-P CSMA
Non-P CSMA
CSMA/CD
a
max
For small a: CSMA-CD has best maximum throughput
For larger a: Aloha & slotted Aloha better maximum throughput, since not dependent on a (normalized propagation delay)

## Slide 41: Unit 02.03.04 CS 5220: COMPUTER COMMUNICATIONS
Scheduling Approaches
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 42: Scheduling for MAC
Schedule frame transmissions to avoid collision in shared medium
  More efficient channel utilization
  Less variability in delays
  Can provide fairness to stations
  Increased computational or procedural complexity
Two main approaches
  Reservation
  Polling

## Slide 43: Collision-free Reservation System
Time
Cycle n
Reservation
interval
Frame
transmissions
r
d
d
d
r
d
d
d
Cycle (n + 1)
r
=
1
2
3
M
Transmissions organized into cycles
Cycle: a reservation interval + frame transmissions

## Slide 44: Reservation Scheme
The reservation interval has a mini-slot for each station to request reservations for frame transmissions
  The stations announce their intention to transmit a frame by broadcasting their reservation bit during the appropriate mini-slot
  By listening to the reservation interval, stations determine the order of frame transmissions in the corresponding cycle
  Mini-slot should cover the round-trip propagation delay
  Collision is avoided

## Slide 45: Example (negligible propagation delay)
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
(a)
8
Initially stations 3 & 5 have reservations to transmit frames
Cycle 3: Station 8 becomes active and makes reservation
Cycle 3: now includes frame transmission from station 8

## Slide 46: Example (non-negligible prop. delay)
Initially stations 3 & 5 have reservations to transmit frames
Cycle 2: Station 8 becomes active and makes reservation
Cycle 3: now includes frame transmission from station 8
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
8
(b)

## Slide 47: Reservation System Options
Centralized or distributed system
  Centralized systems: A central controller listens to reservation information, decides order of transmission, issues grants
  Distributed systems: Each station determines its slot for transmission from the reservation information

## Slide 48: Reservation System Options
Single or Multiple Frames
  Single frame reservation: Only one frame transmission can be reserved within a reservation cycle
  Multiple frame reservation: More than one frame transmission can be reserved within a minoslot
Channelized or Random Access Reservations
  Channelized (typically TDMA) reservation: Reservation messages from different stations are multiplexed without any risk of collision
  Random access reservation: Each station transmits its reservation message randomly until the message goes through

## Slide 49: Efficiency of Reservation Systems
Assume mini-slot duration = vX (v < 1; negligible delay)
A single frame reservation scheme, M stations
  a single frame transmission requires (1+v)X seconds
  Link is fully loaded when all stations transmit, maximum efficiency is:
A k frame reservation scheme
  If k frame transmissions can be reserved with a reservation message and if there are M stations, as many as Mk frames can be transmitted in XM(k+v) seconds
  Maximum efficiency is:

## Slide 50: Random Access Reservation Systems
Large number of light-traffic stations
  Dedicating a minislot to each station is inefficient
Slotted ALOHA reservation scheme
  Stations use slotted Aloha on reservation minislots
  On average, each reservation takes at least e minislot attempts
  Effective time required for the reservation is 2.71vX
X X(1+ev)
1 1 + 2.71v
ρmax = =

## Slide 51: Example: GPRS
General Packet Radio Service
  Packet data service in GSM cellular radio
  GPRS devices, e.g. cellphones or laptops, send packet data over radio and then to Internet
  Slotted Aloha MAC used for reservations
  Single & multi-slot reservations supported

## Slide 52: Polling Systems
Centralized systems: A central controller accepts requests from stations and issues grants to transmit
Distributed systems: Stations implement a decentralized algorithm to determine transmission order
Central
Controller

## Slide 53: Polling System Options
Service Limits: How much is a station allowed to transmit per poll?
  Exhaustive: until station’s data buffer is empty (including new frame arrivals)
  Gated: all data in buffer when poll arrives
  Frame-Limited: one frame per poll
  Time-Limited: up to some maximum time
Priority mechanisms
  More bandwidth and lower delay for stations that appear multiple times in the polling list
  Issue polls for stations with message of priority k or higher

## Slide 54: Comparison of MAC approaches
Channelization
  Feasible if traffic is steady
Aloha & Slotted Aloha
  Simple & quick transfer at very low load
  Accommodates large number of low-traffic bursty users
  Highly variable delay at moderate loads
  Efficiency does not depend on a
CSMA & CSMA-CD
  Quick transfer and high efficiency for low delay-bandwidth product
  Can accommodate large number of bursty users
  Variable and unpredictable delay

## Slide 55: Comparison of MAC approaches (Cont)
Reservation
  On-demand transmission of bursty or steady streams
  Accommodates large number of low-traffic users with slotted Aloha reservations
  Can incorporate QoS
  Handles large delay-bandwidth product via delayed grants
Polling
  Generalization of time-division multiplexing
  Provides fairness through regular access opportunities
  Can provide bounds on access delay
  Performance deteriorates with large delay-bandwidth product

## Slide 56: Typical MAC Efficiencies
CSMA-CD protocol:
Token-ring network
a΄= latency of the ring (bits)/average frame length
Two-Station Example:
If a<<1, then efficiency close to 100%
As a approaches 1, the efficiency becomes low

## Slide 57: Typical Delay-Bandwidth Products
Long and/or fat pipes give large products and a (normalized delay)
Distance | 10 Mbps | 100 Mbps | 1 Gbps | Network Type
1 m | 3.33 x 10-02 | 3.33 x 10-01 | 3.33 x 100 | Desk area network
100 m | 3.33 x 1001 | 3.33 x 1002 | 3.33 x 1003 | Local area network
10 km | 3.33 x 1002 | 3.33 x 1003 | 3.33 x 1004 | Metropolitan area network
1000 km | 3.33 x 1004 | 3.33 x 1005 | 3.33 x 1006 | Wide area network
100000 km | 3.33 x 1006 | 3.33 x 1007 | 3.33 x 1008 | Global area network

## Slide 58: Summary: MAC protocol features
Delay-bandwidth product / normalized delay
Efficiency
Transfer delay
Fairness
Reliability
Capability to carry different types of traffic
Quality of service
Cost