## Slide 1: Unit 02.04.01 CS 5220: COMPUTER COMMUNICATIONS
Local Area Networks (LANs)
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: What is a LAN?
Private ownership
  freedom from regulatory constraints of WANs
Short distance (~1km) between computers
  low cost
  high-speed, relatively error-free communication
  complex error control unnecessary
Machines are constantly moved
  Keeping track of location of computers a chore
  Simply give each machine a unique address
  Broadcast messages to all machines in the LAN
Need a medium access control protocol

## Slide 3: Typical LAN Structure
RAM
RAM
ROM
Ethernet Processor
Transmission Medium
Network Interface Card (NIC)
Unique MAC “physical” address
NIC

## Slide 4: Medium Access Control Sublayer
In IEEE 802.1, Data Link Layer divided into:
Medium Access Control Sublayer
  Coordinate access to medium
  Connectionless frame transfer service
  Machines identified by MAC/physical address
  Broadcast frames with MAC addresses
Logical Link Control Sublayer
  Between Network layer & MAC sublayer

## Slide 5: MAC Sub-layer
Data link
layer
802.3
CSMA-CD
802.5
Token Ring
802.2 Logical link control
Physical
layer
MAC
LLC
802.11
Wireless
LAN
Network layer
Network layer
Physical
layer
OSI
IEEE 802
Various physical layers
Other
LANs

## Slide 6: Logical Link Control Layer
PHY
MAC
PHY
MAC
PHY
MAC
Unreliable Datagram Service
PHY
MAC
PHY
MAC
PHY
MAC
Reliable frame service
LLC
LLC
LLC
A
C
A
C
IEEE 802.2: LLC enhances service provided by MAC

## Slide 7: Logical Link Control Services
Type 1: Unacknowledged connectionless service
  Unnumbered frame mode of HDLC
Type 2: Reliable connection-oriented service
  Asynchronous balanced mode of HDLC
Type 3: Acknowledged connectionless service
Additional addressing
  A workstation has a single MAC physical address
  Can handle several logical connections, distinguished by their SAP (service access points).

## Slide 8: Encapsulation of MAC frames
IP
LLC Header
Data
MAC Header
FCS
LLC PDU
IP Packet

## Slide 9: Ethernet - A bit of history…
1970 ALOHAnet radio network deployed in Hawaiian islands
1973 Metcalf and Boggs invent Ethernet, random access in wired net
1979 DIX Ethernet II Standard
1985 IEEE 802.3 LAN Standard (10 Mbps)
1995 Fast Ethernet (100 Mbps)
1998 Gigabit Ethernet
2002 10 Gigabit Ethernet
Ethernet is dominant LAN standard
Metcalf’s Sketch

## Slide 10: IEEE 802.3 MAC: Ethernet
MAC Protocol: CSMA/CD
Slot Time is the critical system parameter
  upper bound on time to detect collision
  upper bound on time to acquire channel
  upper bound on length of frame segment generated by collision
  quantum for retransmission scheduling
  At least round-trip propagation
Truncated binary exponential backoff
  for n_th retransmission: 0 < r < 2k, where k=min(n,10)
  Give up after 16 retransmissions

## Slide 11: IEEE 802.3 Original Parameters
Transmission Rate: 10 Mbps
Minimum Frame: 512 bits = 64 bytes
Max Length: 2500 meters + 4 repeaters
Slot time: 51.2 msec => 512 bits/10 Mbps
Each x10 increase in bit rate, must be accompanied by x10 decrease in distance, or x10 increase in minimum frame size

## Slide 12: IEEE 802.3 MAC Frame
Preamble
SD
Destination
address
Source
address
Length
Information
Pad
FCS
7
1
6
6
2
4
64 - 1518 bytes
Synch
Start
frame
802.3 MAC Frame
Every frame transmission begins “from scratch”
Preamble helps receivers synchronize their clocks to transmitter clock
7 bytes of 10101010 generate a square wave
Start frame byte changes to 10101011
Receivers look for change in 10 pattern

## Slide 13: IEEE 802.3 MAC Frame
Preamble
SD
Destination
address
Source
address
Length
Information
Pad
FCS
7
1
6
6
2
4
64 - 1518 bytes
Synch
Start
frame
0
Single address
1
Group address
Destination address
  single address
  group address
  broadcast = 111...111
Addresses
  local or global
Global addresses
0
Local address
1
Global address
802.3 MAC Frame

## Slide 14: IEEE 802.3 MAC Frame
Preamble
SD
Destination
address
Source
address
Length
Information
Pad
FCS
7
1
6
6
2
4
64 - 1518 bytes
Synch
Start
frame
802.3 MAC Frame
Length: # bytes in information field
  Max frame 1518 bytes, excluding preamble & SD
  Max information 1500 bytes: 05DC
Pad: ensures minimum frame of 64 bytes
FCS: CCITT-32 CRC, covers addresses, length, information, pad fields
  NIC discards frames if failed CRC

## Slide 15: Ethernet Scalability
CSMA-CD maximum throughput depends on the normalized delay-bandwidth product a=tprop/X (X is the frame transmission time)
x10 increase in bit rate = x10 decrease in X
To keep a constant need to either: decrease tprop (distance) by x10; or increase frame length x10

## Slide 16: Fast Ethernet
 | 100baseT4 | 100baseT | 100baseFX
Medium | Twisted pair category 3 UTP 4 pairs | Twisted pair category 5 UTP two pairs | Optical fiber multimode Two strands
Max. Segment Length | 100 m | 100 m | 2 km
Topology | Star | Star | Star
Table 6.4 IEEE 802.3 100 Mbps Ethernet medium alternatives
To preserve compatibility with 10 Mbps Ethernet:
Same frame format, same interfaces, same protocols
Hub topology only with twisted pair & fiber
Bus topology & coaxial cable abandoned

## Slide 17: Gigabit Ethernet
Table 6.3 IEEE 802.3 1 Gbps Fast Ethernet medium alternatives
 | 1000baseSX | 1000baseLX | 1000baseCX | 1000baseT
Medium | Optical fiber multimode Two strands | Optical fiber single mode Two strands | Shielded copper cable | Twisted pair category 5 UTP
Max. Segment Length | 550 m | 5 km | 25 m | 100 m
Topology | Star | Star | Star | Star
Slot time increased to 512 bytes; small frames need to be extended to 512 Bytes
Frame bursting to allow stations to transmit burst of short frames
Frame structure preserved but CSMA-CD essentially abandoned, and operated primarily in a switched mode
Extensive deployment in backbone of enterprise data networks and server farms

## Slide 18: 10 Gigabit Ethernet
Table 6.5 IEEE 802.3 10 Gbps Ethernet medium alternatives
 | 10GbaseSR | 10GBaseLR | 10GbaseEW | 10GbaseLX4
Medium | Two optical fibers Multimode at 850 nm 64B66B code | Two optical fibers Single-mode at 1310 nm 64B66B | Two optical fibers Single-mode at 1550 nm SONET compatibility | Two optical fibers multimode/single-mode with four wavelengths at 1310 nm band 8B10B code
Max. Segment Length | 300 m | 10 km | 40 km | 300 m – 10 km
Frame structure preserved
CSMA-CD protocol officially abandoned
LAN PHY for local network applications
WAN PHY for wide area interconnection using SONET OC-192c
Extensive deployment in metro networks and in datacenters

## Slide 19: Unit 02.04.02 CS 5220: COMPUTER COMMUNICATIONS
Wireless LANs: CSMA-CA
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 20: Wireless Data Communications
Wireless communication is compelling
  Easy, low-cost deployment
  Mobility & roaming: Access information anywhere
  Supports personal devices
    PDAs, laptops, data-cell-phones
  Supports communicating devices
    Cameras, location devices, wireless identification
  Susceptible to noise and interference: reliability!
  Signal strength varies in space & time: coverage!
  Signal can be captured by snoopers: security!

## Slide 21: Hidden Terminal Problem
A transmits data frame
(a)
Data Frame
Data Frame
A
B
C
C transmits data frame & collides with A at B
(b)
C senses medium,
station A is hidden from C
Data Frame
B
C
A

## Slide 22: CSMA-CA
RTS
CTS
CTS
Data Frame
A requests to send
B
C
A
A sends
B
B
C
C remains quiet
B announces A ok to send
(a)
(b)
(c)
ACK
B
(d)
ACK
B sends ACK

## Slide 23: Ad Hoc Communications
B
D
C
A
An ad-hoc network: temporary association of group of stations
  Within range of each other; Need to exchange information
  E.g. Presentation in meeting, or distributed computer game, or both
The basic service set (BSS)
The basic service area (BSA)

## Slide 24: Infrastructure Network
A2
B2
B1
A1
AP1
AP2
Distribution System
Server
Gateway to
the Internet
Portal
Portal
BSS A
BSS B

## Slide 25: IEEE 802.11 Wireless LAN
Stimulated by availability of unlicensed spectrum
  U.S. Industrial, Scientific, Medical (ISM) bands
  902-928 MHz, 2.400-2.4835 GHz, 5.725-5.850 GHz
Targeted wireless LANs @ 20 Mbps
MAC for high speed wireless LAN
Ad Hoc & Infrastructure networks
Variety of physical layers

## Slide 26: 802.11 Definitions
Basic Service Set (BSS)
  Group of stations that coordinate their access using a given instance of MAC
  Located in a Basic Service Area (BSA)
  Stations in BSS can communicate with each other
  Distinct collocated BSS’s can coexist
Extended Service Set (ESS)
  Multiple BSSs interconnected by Distribution System (DS)
  Each BSS is like a cell and stations in BSS communicate with an Access Point (AP)
  Portals (access point) attached to DS provide access to Internet

## Slide 27: Distribution Services
Stations in BSS can communicate directly with each other
DS provides distribution services:
  Transfer MSDUs between APs in ESS
  Transfer MSDUs between portals & BSSs in ESS
  Transfer MSDUs between stations in same BSS
    Multicast, broadcast, or stations’s preference
ESS looks like single BSS to LLC layer

## Slide 28: Infrastructure Services
Select AP and establish association with AP
  Then can send/receive frames via AP & DS
Reassociation service to move from one AP to another AP
Dissociation service to terminate association
Authentication service to establish identity of other stations
Privacy service to keep contents secret

## Slide 29: Frame Types
Management frames
  Station association & disassociation with AP
  Timing & synchronization
  Authentication & de-authentication
Control frames
  Handshaking
  ACKs during data transfer
Data frames
  Data transfer

## Slide 30: Frame Structure
Address
2
Frame
Control
Duration/
ID
Address
1
Address
3
Sequence
control
Address
4
Frame
body
CRC
2
2
6
6
6
2
6
0-2312
4
MAC header (bytes)
MAC Header: 30 bytes
Frame Body: 0-2312 bytes
CRC: CCITT-32 4 bytes CRC over MAC header & frame body

## Slide 31: Summary: IEEE 802.11 Physical Layer Options
 | Frequency Band | Bit Rate | Modulation Scheme
802.11 | 2.4 GHz | 1-2 Mbps | Frequency-Hopping Spread Spectrum, Direct Sequence Spread Spectrum
802.11b | 2.4 GHz | 11 Mbps | Complementary Code Keying & QPSK
802.11g | 2.4 GHz | 54 Mbps | Orthogonal Frequency Division Multiplexing & CCK for backward compatibility with 802.11b
802.11a | 5-6 GHz | 54 Mbps | Orthogonal Frequency Division Multiplexing

## Slide 32: Unit 02.04.03 CS 5220: COMPUTER COMMUNICATIONS
Wireless LANs: Medium Access Control
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 33: IEEE 802.11 MAC
MAC sublayer responsibilities
  Channel access
  PDU addressing, formatting, error checking
  Fragmentation & reassembly of MAC SDUs
MAC security service options
  Authentication & privacy
MAC management services
  Roaming within ESS
  Power management

## Slide 34: MAC Services
DCF Contention Service: Asynchronous best-effort, required for all stations
PCF Contention-Free Service: connection-oriented, time-bounded transfer
MAC can alternate between Contention Periods (CPs) & Contention-Free Periods (CFPs)
Physical
Distribution coordination function
(CSMA-CA)
Point coordination
function
Contention-free service
Contention service
MAC
MSDUs
MSDUs

## Slide 35: Distributed Coordination Function (DCF)
CSMA-CA (carrier sense multiple access with collision avoidance)
  Ready stations wait for completion of transmission
  All stations must wait Interframe Space (IFS)
DIFS
DIFS
PIFS
SIFS
Contention
window
Next frame
Defer access
Wait for
reattempt time
Time
Busy medium

## Slide 36: Priorities through Interframe Spacing
High-Priority frames wait Short IFS (SIFS)
  Typically to complete exchange in progress
  ACKs, CTS, data frames of segmented MSDU, etc.
PCF IFS (PIFS) to initiate Contention-Free Periods
DCF IFS (DIFS) to transmit data & MPDUs
DIFS
DIFS
PIFS
SIFS
Contention
window
Next frame
Defer access
Wait for
reattempt time
Time
Busy medium

## Slide 37: Contention & Backoff Behavior
If channel is still idle after DIFS period, ready station can transmit an initial MPDU
If channel becomes busy before DIFS, then station must schedule backoff time for reattempt
  Backoff period is integer # of idle contention time slots
  Waiting station monitors medium & decrements backoff timer each time an idle contention slot transpires
  Station can contend when backoff timer expires
A station that completes a frame transmission is not allowed to transmit immediately
  Must first perform a backoff procedure

## Slide 38: Carrier Sensing in 802.11
Physical Carrier Sensing
  Analyze all detected frames
  Monitor relative signal strength from other sources
Virtual Carrier Sensing at MAC sublayer
  Source stations informs other stations of transmission time (in msec) for an MPDU
  Carried in Duration field of RTS & CTS
  Stations adjust Network Allocation Vector to indicate when channel will become idle
Channel busy if either sensing is busy

## Slide 39: Transmission of MPDU without RTS/CTS
Data
DIFS
SIFS
Defer Access
Wait for Reattempt Time
ACK
DIFS
NAV
Source
Destination
Other

## Slide 40: Transmission of MPDU with RTS/CTS
Data
SIFS
Defer access
Ack
DIFS
NAV (RTS)
Source
Destination
Other
RTS
DIFS
SIFS
CTS
SIFS
NAV (CTS)
NAV (Data)

## Slide 41: Collisions, Losses & Errors
Collision Avoidance
  When station senses channel busy, it waits until channel becomes idle for DIFS period & then begins random backoff time (in units of idle slots)
  Station transmits frame when backoff timer expires
  If collision, recompute backoff over interval that is twice as long
Receiving stations of error-free frames send ACK
  Sending station interprets non-arrival of ACK as loss
  Executes backoff and then retransmits
  Receiving stations use sequence numbers to identify duplicate frames

## Slide 42: Point Coordination Function
Point coordinator (PC) in AP performs PCF
Polling table up to implementor
CFP repetition interval
  Determines frequency with which CFP occurs
  Initiated by beacon frame transmitted by PC in AP
  Contains CFP and CP
  During CFP stations may only transmit to respond to a poll from PC or to send ACK

## Slide 43: SUMMARY
Distributed Coordination Function DCF is required
Point Coordination Function PCF is optional