## Slide 1: Unit 03.01.01 CS 5220: COMPUTER COMMUNICATIONS
Bridges and Data Link Layer Switching
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Interconnecting Networks
Several ways of interconnecting networks
Application layer Application gateway
Transport layer Transport gateway
Network layer Router
Data Link layer Bridge, Switch
Physical layer Repeater, Hub

## Slide 3: Hubs, Bridges & Routers
Hub: Active central element in a star topology
  Twisted Pair: inexpensive, easy to install
  Simple repeater in Ethernet LANs
  “Intelligent hub”: fault isolation, net configuration, statistics
  User community grows, need to interconnect hubs:
Hub
Station
Station
Station
Two Twisted
Pairs
Hub
Station
Station
Station
Two Twisted
Pairs
?
Hub

## Slide 4: Hubs, Bridges & Routers
Interconnecting Hubs/LANs
  Repeater: Signal regeneration
    All traffic appears in both LANs
  Bridge: MAC address filtering
    Local traffic stays in own LAN
  Routers: Internet routing
    All traffic stays in own LAN
Higher
Scalability

## Slide 5: General Bridge Issues
Operation at data link level implies capability to work with multiple network layers; However, must deal with
  Difference in MAC formats, and maximum frame length
  Difference in data rates; buffering; timers; security
PHY
MAC
LLC
Network
Network
PHY
MAC
LLC
802.3
802.3
802.5
802.5
802.3
802.3
802.3
802.5
802.5
802.5
CSMA/CD
Token Ring

## Slide 6: Bridges of Same Type
Bridge
Network
Physical
Network
LLC
Physical
Physical
Physical
LLC
MAC
MAC
MAC
MAC
Common case involves LANs of same type
Bridging is done at MAC level
Notes: Two types of bridges are widely used: transparent bridges and source routing bridges.
Transparent bridges are typically used in Ethernet
source routing bridges are typically used in token ring and FTTI networks.

## Slide 7: Transparent Bridges
Interconnection of IEEE LANs with complete transparency
Use backward learning to build table
  observe source address of arriving frame
  handle topology changes by removing old entries
Use table lookup, and
  discard frame, if source & destination in same LAN
  forward frame, if source & destination in different LAN
  use flooding, if destination unknown
Bridge
S1
S2
S4
S3
S5
S6
LAN1
LAN2
Notes: A transparent bridge's duties include
Forwarding
Blocking
Filtering frame

## Slide 8: S1→S5
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
Address Port
S1 to S5

## Slide 9: S1→S5
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
Address Port
S1
1
S1 to S5

## Slide 10: S1→S5
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
Address Port
S1
1
S1 to S5

## Slide 11: S1→S5
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
Address Port
S1
1
S1 to S5

## Slide 12: S3→S2
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
Address Port
S1
1
S3S2

## Slide 13: S3→S2
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
Address Port
S1
1
S3
2
S3S2
S3S2
S3
1

## Slide 14: S3→S2
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
S3
1
Address Port
S1
1
S3
2
S3S2
S3S2

## Slide 15: S4S3
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
S4 S3
Address Port
S1
1
S3
2
Address Port
S1
1
S3
1
S4S3

## Slide 16: S4S3
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
S4 S3
Address Port
S1
1
S3
2
Address Port
S1
1
S3
1
S4
2
S4S3

## Slide 17: S4S3
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
S4 S3
Address Port
S1
1
S3
2
S4
2
Address Port
S1
1
S3
1
S4
2
S4S3

## Slide 18: S2S1
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
S3
2
S4
2
Address Port
S1
1
S3
1
S4
2
S2S1

## Slide 19: S2S1
B1
S1
S2
B2
S3
S4
S5
Port 1
Port 2
Port 1
Port 2
LAN1
LAN2
LAN3
Address Port
S1
1
S3
2
S4
2
S2
1
Address Port
S1
1
S3
1
S4
2
S2S1

## Slide 20: Summary: Adaptive Learning
In a static network, tables eventually store all addresses & learning stops
In practice, stations are added & moved all the time
  Introduce timer (minutes) to age each entry & force it to be relearned periodically
  If frame arrives on port that differs from frame address & port in table, update immediately
  Spanning tree algorithm is adopted to avoid loops in interconnection

## Slide 21: Unit 03.01.02 CS 5220: COMPUTER COMMUNICATIONS
Network Layer Services and Topology
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 22: Network Layer
Network Layer: the most complex layer
  Requires the coordinated actions of multiple, geographically distributed network elements (switches & routers)
  Must be able to deal with very large scales
    Billions of users (people & communicating devices)
  Biggest Challenges
    Addressing: where should information be directed to?
    Routing: what path should be used to get information there?

## Slide 23: Packet Switching
t0
t1
Network
Transfer of information as payload in data packets
Packets undergo random delays & possible loss
Different applications impose differing requirements on the transfer of information

## Slide 24
End system
β
Physical
layer
Data link
layer
Physical
layer
Data link
layer
End system
α
Network
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Physical
layer
Data link
layer
Network
layer
Transport
layer
Transport
layer
Messages
Messages
Segments
Network
service
Network
service
Network Service
Network layer can offer a variety of services to transport layer

## Slide 25: Network Service vs. Operation
Network Service
Connectionless
  Datagram Transfer
Connection-Oriented
  Reliable and possibly constant bit rate transfer
Internal Network Operation
Connectionless
  IP
Connection-Oriented
  ATM
Various combinations are possible
Connection-oriented service over Connectionless operation
Connectionless service over Connection-Oriented operation
Context & requirements determine what makes sense

## Slide 26: Complexity at the Edge or in the Core?
1
1
3
3
2
1
2
2
3
2
1
1
2
2
1
2
1
Medium
A
B
3
2
1
1
2
2
1
C
2
1
2
1
2
1
4
1
2
3
4
End system α
End system β
Network
1
2
Physical layer entity
Data link layer entity
3
Network layer entity
3
Network layer entity
Transport layer entity
4

## Slide 27: The End-to-End Argument for System Design
An end-to-end function is best implemented at a higher level than at a lower level
  End-to-end service requires all intermediate components to work properly
  Higher-level better positioned to ensure correct operation
Example: stream transfer service
  Establishing an explicit connection for each stream across network requires all network elements (NEs) to be aware of connection; All NEs have to be involved in re-establishment of connections in case of network fault
  In connectionless network operation, NEs do not deal with each explicit connection and are much simpler in design

## Slide 28: Network Layer Functions
Essentials
Routing: mechanisms for determining the set of best paths for routing packets that requires the collaboration of network elements
Forwarding: transfer of packets from inputs to outputs
Priority & Scheduling: determining order of packet transmission in each network element
Optional: congestion control, segmentation & reassembly, security

## Slide 29: End-to-End Packet Network Topology
In Packet networks,
Individual packet streams are highly bursty
  Statistical multiplexing is used to concentrate streams
User demand can undergo dramatic change
  Peer-to-peer applications stimulated huge growth in traffic volumes
Internet structure highly decentralized
  Paths traversed by packets can go through many networks controlled by different organizations
  No single entity responsible for end-to-end service

## Slide 30: Access Multiplexing
Access
MUX
To
packet
network
Packet traffic from users multiplexed at access to network into aggregated streams
DSL traffic multiplexed at DSL Access Mux
Cable modem traffic multiplexed at Cable Modem Termination System
Notes: The main purpose of the access and multiplexer is to combine the typically
bursty traffic flows from the individual computers into aggregated flows,
so that the transmission lines to the packet network is used more efficiently.
______________________________________________________
Digital Subscriber Line.
Users get a high speed bandwidth connection from
a phone wall jack on an existing telephone network.
DSL works within the frequencies that the telephone
doesn't so you can use the Internet while making phone calls.

## Slide 31: Oversubscription
Access Multiplexer
  N subscribers connected @ c bps to mux
  Each subscriber active r/c of time
  Mux has C = mc bps to network
  Oversubscription ratio: N/m
  Find m so that at most 1% overflow probability
• • •
Nr
Nc
r
r
r
mc
• • •
Notes: there are N subscribers to the multiplexer each with the maxim bandwidth C (bps)
So aggregated maxim bandwidth of all subscribers is therefore N times C,

## Slide 32
Feasible oversubscription rate increases with size
N | r/c | m | N/m | 
10 | 0.01 | 1 | 10 | 10 extremely lightly loaded users
10 | 0.05 | 3 | 3.3 | 10 very lightly loaded user
10 | 0.1 | 4 | 2.5 | 10 lightly loaded users
20 | 0.1 | 6 | 3.3 | 20 lightly loaded users
40 | 0.1 | 9 | 4.4 | 40 lightly loaded users
100 | 0.1 | 18 | 5.5 | 100 lightly loaded users
• • •
Nr
Nc
r
r
r
mc
• • •
Oversubscription Ratio

## Slide 33: Home LANs
Home Router
  LAN Access using Ethernet or WiFi (IEEE 802.11)
  Private IP addresses in Home (192.168.0.x) using Network Address Translation (NAT)
  Single global IP address from ISP issued using Dynamic Host Configuration Protocol (DHCP)
Home
Router
To
packet
network
WiFi
Ethernet

## Slide 34: LAN Concentration
LAN Hubs and switches in the access network also aggregate packet streams that flows into switches and routers
     
     
Switch
/ Router

## Slide 35: Campus Network
R
R
R
R
S
S
S
s
s
s
s
s
s
s
s
s
s
R
s
R
Backbone
To Internet or wide area network
Organization Servers
Departmental Server
Gateway
Only outgoing packets leave LAN through router
High-speed campus backbone net connects dept routers
Servers have redundant connectivity to backbone

## Slide 36: Summary:
End-to-end argument significantly affect networking system design, for performance and scalability
Oversubscription is a common technique with multiplexing for efficiency

## Slide 37: Unit 03.01.03 CS 5220: COMPUTER COMMUNICATIONS
Packet Switching - Datagrams
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 38: The Switching Function
Dynamic interconnection of inputs to outputs
Enables dynamic sharing of transmission resource
Two fundamental approaches:
  Connectionless
  Connection-Oriented
Backbone Network
Access Network
Switch

## Slide 39: Packet Switching Network
Packet
switch
Network
Transmission
line
User
Packet switching network
Transfers packets between users
Transmission lines + packet switches (routers)
Origin in message switching
Two modes of operation:
Connectionless
Virtual Circuit
Notes: 7-9
The text boxes are callouts or labels.

## Slide 40: Message Switching
Message switching invented for telegraphy
Entire messages multiplexed onto shared lines, stored & forward
Headers for source & destination addresses
Routing at message switches
Connectionless
Switches
Message
Destination
Source
Message
Message
Message
Transmission delay vs. propagation delay
Transmit a 1000B from LA to DC via a 1Gbps network, signal speed 200Km/sec.
Notes: Overall delay = tranmisssion delay + propagation delay

## Slide 41: Message Switching Delay
t
t
t
t
Delay
Source
Destination
T

Minimum delay = 3 + 3T
Switch 1
Switch 2
Additional queueing delays possible at each link
Notes: τ: propagation delay
T: transmission delay

## Slide 42: Long Messages vs. Packets
Approach 1: send 1 Mbit message
Probability message arrives correctly
On average it takes about 3 transmissions/hop
Total # bits transmitted ≈ 6 Mbits
1 Mbit
message
source
dest
BER=p=10-6
BER=10-6
How many bits need to be transmitted to deliver message?
Approach 2: send 10 100-kbit packets
Probability packet arrives correctly
On average it takes about 1.1 transmissions/hop
Total # bits transmitted ≈ 2.2 Mbits
Pc = (1 – 10-6)10^6 ≈ e -10^6 10^-6 = e-1 ≈ 1/3
Pc = (1 – 10-6)10^5 ≈ e -10^5 10^-6 = e-1/10 ≈ 0.9
Notes: BER: bit error rate

## Slide 43: Packet Switching - Datagram
Messages broken into smaller units (packets)
Source & destination addresses in packet header
Connectionless, packets routed independently (datagram)
Packet may be out of order
Pipelining of packets across network can reduce delay, increase throughput
Lower delay than message switching, suitable for interactive traffic
Packet 2
Packet 1
Packet 1
Packet 2
Packet 2

## Slide 44: Packet Switching Delay
t
t
t
t
Delay
3
1
2
3
1
2
3
2
1
Minimum Delay = 3τ + 5(T/3) (assumed single path, no queueing delay)
Packet pipelining enables message to arrive sooner
Assume three packets corresponding to one message
1/3T
Switch 1
Switch 2
Source
Destination
Notes: τ: propagation delay
T: transmission delay

## Slide 45: Delay for k-Packet Message over L Hops
t
t
t
t
3
1
2
3
1
2
3
2
1
3 + 2(T/3) first bit received
3 + 3(T/3) first bit released
3 + 5 (T/3) last bit released
L + (L-1)P first bit received
L + LP first bit released
L + LP + (k-1)P last bit released
where T = k P
3 hops
L hops
Source
Destination
Switch 1
Switch 2


## Slide 46: Summary:
Long message switching suffers long delay and is more vulnerable to errors.
Packet pipelining reduce delay and improve throughput.