## Slide 1: Unit 03.02.01 CS 5220: COMPUTER COMMUNICATIONS
Packet Switching – Virtual Circuits
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Packet Switching – Virtual Circuit
Call set-up phase sets ups pointers in fixed path along networks
All packets for a connection follow the same path
Abbreviated header identifies connection on each link
Variable bit rates possible, negotiated during call set-up
Physical-layer circuit vs Network-layer virtual circuit
Virtual circuit
Packet
Packet
Packet
Packet

## Slide 3: Connection Setup
SW 1
SW 2
SW n
Connect request
Connect request
Connect request
Connect confirm
Connect confirm
Connect confirm
…
Signaling messages propagate as route is selected
Signaling messages identify connection and setup tables in switches
Typically a connection is identified by a local tag, Virtual Circuit Identifier (VCI)
Each switch only needs to know how to relate an incoming tag in one input to an outgoing tag in the corresponding output
Once tables are setup, packets can flow along path

## Slide 4: Virtual Circuit Forwarding Tables
Input
VCI
Output
port
Output
VCI
15
15
58
13
13
7
27
12
44
23
16
34
Each input port of packet switch has a forwarding table
Lookup entry for per-link/port VCI of incoming packet
Determine output port (next hop) and insert VCI for next link
Very high speeds are possible (HW-based)
Table can also include priority or other information about how packet should be treated

## Slide 5: Routing in Virtual Circuit Subnet
Label switching

## Slide 6: Virtual Circuit w/ Connection Setup Delay
t
t
t
t
3
1
2
3
1
2
3
2
1
Release
Connect request
CR
CR
Connect confirm
CC
CC
Connection setup delay is incurred before any packet can be transferred
Delay is acceptable for sustained transfer of large number of packets
This delay may be unacceptably high if only a few packets are being transferred

## Slide 7: Example: ATM Networks
All information mapped into short fixed-length packets called cells
Connections set up across network
  Virtual circuits established across networks
  Tables setup at ATM switches
Several types of network services offered
  Constant bit rate connections
  Variable bit rate connections

## Slide 8: Cut-Through Switching
3
1
2
3
1
2
3
2
1
Minimum delay = 3 + T
t
t
t
t
Source
Destination
Switch 1
Switch 2
Some networks perform error checking on header only, so packets can be forwarded as soon as header is received & processed
Delays reduced further with cut-through switching

## Slide 9: Message vs. Packet Minimum Delay
Message switching:
  L t + L T = L t + (L – 1) T + T
Packet switching with store-and-forward
  L t + L P + (k – 1) P = L t + (L – 1) P + T
Cut-Through Packet switching (Immediate forwarding after header) = L t + T
  Above measurements neglect header processing delays

## Slide 10
5-4

## Slide 11: Unit 03.02.02 CS 5220: COMPUTER COMMUNICATIONS
Routing in Packet Networks
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 12: Routing in Packet Networks
1
2
3
4
5
6
Node
(switch or router)
Three possible (loopfree) routes from 1 to 6:
  1-3-6, 1-4-5-6, 1-2-5-6
Which is “best”?
  Min delay? Min hop? Max bandwidth? Min cost?

## Slide 13: Routing Algorithm Requirements
Responsiveness to changes
  Topology or bandwidth changes, congestion
  Rapid convergence of routers to consistent set of routes
  Freedom from persistent loops
Optimality
  Resource utilization, path length
Robustness
  Continues working under high load, congestion, faults, equipment failures, incorrect implementations
Simplicity
  Efficient software implementation, reasonable processing load

## Slide 14: Creating the Routing Tables
Need information on state of links
  Link up/down; congested; delay or other metrics
Need to distribute link state info using a routing protocol
  What information is exchanged? How often?
  Exchange with neighbors; Broadcast or flood
Need to compute routes based on information
  Single metric; multiple metrics
  Single route; alternate routes

## Slide 15: Routing Tables in Datagram Networks
Destination
address
Output
port
1345
12
2458
7
0785
6
12
1566
Route determined by table lookup
Routing decision involves finding next hop in route to given destination
Routing table has an entry for each destination specifying output port that leads to next hop
Size of table becomes impractical for very large number of destinations
Notes: (Destination, next hop, cost)

## Slide 16: Example: Internet Routing
Internet protocol uses datagram packet switching across networks
  Networks are treated as data links
Hosts have two-part IP address:
  Network address + Host address
Routers do table lookup on network address
  This reduces size of routing table
In addition, network addresses are assigned so that they can also be aggregated

## Slide 17: Routing in Virtual-Circuit Packet Networks
1
2
3
4
5
6
A
B
C
D
1
5
2
3
7
1
8
5
4
2
3
6
5
2
Switch or router
Host
VCI
Route determined during connection setup
Tables in switches implement forwarding that realizes selected route

## Slide 18: Non-Hierarchical Addresses and Routing
0000 0111 1010 1101
0001 0100 1011 1110
0011 0101 1000 1111
0011 0110 1001 1100
R1
1
2
5
4
3
0000 1 0111 1 1010 1 … …
0001 4 0100 4 1011 4 … …
R2
No relationship between addresses & routing proximity
Routing tables require 16 entries each

## Slide 19: Hierarchical Addresses and Routing
0000 0001 0010 0011
0100 0101 0110 0111
1100 1101 1110 1111
1000 1001 1010 1011
R1
R2
1
2
5
4
3
00 1 01 3 10 2 11 3
00 3 01 4 10 3 11 5
Prefix indicates network where host is attached
Routing tables require 4 entries each

## Slide 20: Specialized Routing
Flooding
  Useful in starting up network
  Useful in propagating information to all nodes
Deflection Routing
  Fixed, preset routing procedure
  No route synthesis
Notes: Synthesis: tổng hợp
Không tổng hợp tuyến đường

## Slide 21: Flooding
Send a packet to all nodes in a network
No routing tables available
Need to broadcast packet to all nodes (e.g. to propagate link state information)
Approach
Send packet on all ports except one where it arrived
Exponential growth in packet transmissions

## Slide 22
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 1 transmissions

## Slide 23
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 2 transmissions

## Slide 24
1
2
3
4
5
6
Flooding is initiated from Node 1: Hop 3 transmissions

## Slide 25: Limited Flooding
Time-to-Live field in each packet limits number of hops to certain diameter
Each router adds its ID before flooding; discards repeats
Source puts sequence number in each packet; switches records source address and sequence number and discards repeats

## Slide 26: Deflection Routing
Network nodes forward packets to preferred port
If preferred port busy, deflect packet to another port
Works well with regular topologies
  Manhattan street network
  Rectangular array of nodes
  Nodes designated (i,j)
  Rows alternate as one-way streets
  Columns alternate as one-way avenues
Bufferless operation is possible
  Proposed for optical packet networks
  All-optical buffering currently not viable

## Slide 27
0,0
0,1
0,2
0,3
1,0
1,1
1,2
1,3
2,0
2,1
2,2
2,3
3,0
3,1
3,2
3,3
Tunnel from last column to first column or vice versa
Manhattan Street Network

## Slide 28: Summary:
Routing algorithm optimality depends on the objective function that the network operator tries to optimize
Hierarchical addressing reduces the size of routing table
Flooding is useful when routing tables are unavailable

## Slide 29: Unit 03.02.03 CS 5220: COMPUTER COMMUNICATIONS
Shortest Path Routing – Distance Vector
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 30: Shortest Paths & Routing
Many possible paths connect any given source and to any given destination
Routing involves the selection of the path to be used to accomplish a given transfer
Typically it is possible to attach a cost or distance to a link connecting two nodes
Routing can then be posed as a shortest path problem

## Slide 31: Routing Metrics
Means for measuring desirability of a path
Path Length = sum of costs or distances
Possible metrics
  Hop count: rough measure of resources used
  Reliability: link availability; BER
  Delay: sum of delays along path; complex & dynamic
  Bandwidth: “available capacity” in a path
  Load: Link & router utilization along path
  Cost: $$$
Notes: Số liệu định tuyến

## Slide 32: Shortest Path Approaches
Distance Vector Protocols
Neighbors exchange list of distances to destinations
Best next-hop determined for each destination
Bellman-Ford (distributed) shortest path algorithm
Link State Protocols
Link state information flooded to all routers
Routers have complete topology information
Shortest path (& hence next hop) calculated
Dijkstra (centralized) shortest path algorithm

## Slide 33: Distance Vector Do you know the way to San Jose?
San Jose 392
San Jose 596
San Jose 294
San Jose 250

## Slide 34: Distance Vector
Local Signpost
Direction
Distance
Routing Table
For each destination list:
Next Node
Distance
Table Synthesis
Neighbors exchange table entries
Determine current best next hop
Inform neighbors
  Periodically
  After changes
dest
next
dist

## Slide 35: Shortest Path to SJ
i
j
San
Jose
Cij
Dj
Di
If Di is the shortest distance to SJ from i
and if j is a neighbor on the shortest path, then Di = Cij + Dj
Focus on how nodes find their shortest path to a given destination node, i.e. SJ

## Slide 36: But we don’t know the shortest paths
Router i only has local info
from neighbors
Dj"
Cij”
i
San
Jose
j
Cij
Dj
Di
j"
Cij'
j'
Dj'
Pick current
shortest path

## Slide 37: How Distance Vector Works
San
Jose
1 Hop
From SJ
2 Hops
From SJ
3 Hops
From SJ

## Slide 38: How Distance Vector Works
San
Jose
1 Hop
From SJ
2 Hops
From SJ
3 Hops
From SJ
SJ sends
accurate info

## Slide 39: How Distance Vector Works
San
Jose
1 Hop
From SJ
2 Hops
From SJ
3 Hops
From SJ
Hop-1 nodes
calculate current
(next hop, dist), &
send to neighbors

## Slide 40
Jack Dark
1 Hop
From SJ
2 Hops
From SJ
3 Hops
From SJ
Current info about SJ
ripples across network,
Shortest Path Converges

## Slide 41: Bellman-Ford Algorithm
Consider computations for one destination d
Initialization
  Each node table has 1 row for destination d
  Distance of node d to itself is zero: Dd=0
  Distance of other node j to d is infinite: Dj=, for j d
  Next hop node nj = -1 to indicate not yet defined for j  d
Send Step
  Send new distance vector to immediate neighbors across local link
Receive Step
  At node j, find the next hop that gives the minimum distance to d,
    Minj { Cij + Dj }
    Replace old (nj, Dj(d)) by new (nj*, Dj*(d)) if new next node or distance
  Go to send step

## Slide 42
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
San
Jose
Table entry
@ node 1
for dest SJ
Table entry
@ node 3
for dest SJ

## Slide 43
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6,1) | (-1, ) | (6,2)
2 |  |  |  |  | 
3 |  |  |  |  | 
San
Jose
D6=0
D3=D6+1
n3=6
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
D6=0
D5=D6+2
n5=6
0
2
1

## Slide 44
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6, 1) | (-1, ) | (6,2)
2 | (3,3) | (5,6) | (6, 1) | (3,3) | (6,2)
3 |  |  |  |  | 
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
1
2
3
3
6

## Slide 45
Iteration | Node 1 | Node 2 | Node 3 | Node 4 | Node 5
Initial | (-1, ) | (-1, ) | (-1, ) | (-1, ) | (-1, )
1 | (-1, ) | (-1, ) | (6, 1) | (-1, ) | (6,2)
2 | (3,3) | (5,6) | (6, 1) | (3,3) | (6,2)
3 | (3,3) | (4,4) | (6, 1) | (3,3) | (6,2)
San
Jose
3
1
5
4
6
2
2
3
4
2
1
1
2
3
5
0
1
2
6
3
3
4

## Slide 46
San
Jose
3
1
5
4
6
2
2
2
1
1
2
3
5
0
1
2
6
3
3
Summary: Shortest-Path Tree