## Slide 1: Unit 03.03.01 CS 5220: COMPUTER COMMUNICATIONS
Shortest Path Routing – Link State
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Counting to Infinity Problem
3
1
2
4
1
1
1
3
1
2
4
1
1
X
(a)
(b)
Destination/root is node 4; link (3,4) fails.

## Slide 3: Counting to Infinity Problem (Cont.)
Update | Node 1 | Node 2 | Node 3
Before break | (2,3) | (3,2) | (4, 1)
After break | (2,3) | (3,2) | (2,3)
1 | (2,3) | (3,4) | (2,3)
2 | (2,5) | (3,4) | (2,5)
3 | (2,5) | (3,6) | (2,5)
4 | (2,7) | (3,6) | (2,7)
5 | (2,7) | (3,8) | (2,7)
… | … | … | …
Nodes 2 and 3 believe best path is through each other (Destination is node 4)

## Slide 4: Problem: Bad News Travels Slowly
Remedies
Split Horizon
  Do not report route to a destination to the neighbor from which route was learned
Split Horizon with Poisoned Reverse
  Report route to a destination to the neighbor from which route was learned, but with infinite distance
  Breaks erroneous direct loops immediately
  Does not work on some indirect loops

## Slide 5: Split Horizon with Poison Reverse
3
1
2
4
1
1
1
3
1
2
4
1
1
X
(a)
(b)
Destination is node 4
Update | Node 1 | Node 2 | Node 3 | 
Before break | (2, 3) | (3, 2) | (4, 1) | 
After break | (2, 3) | (3, 2) | (-1, ) | Node 2 advertizes its route to 4 to node 3 as having distance infinity; node 3 finds there is no route to 4
1 | (2, 3) | (-1, ) | (-1, ) | Node 1 advertizes its route to 4 to node 2 as having distance infinity; node 2 finds there is no route to 4
2 | (-1, ) | (-1, ) | (-1, ) | Node 1 finds there is no route to 4
Notes: Advertizes ~ inform

## Slide 6: Link-State Algorithm
Basic idea: three step procedure
  Each source node creates a link state packet containing to-neighbor link metrics
  Each source node broadcasts its link state packet so as to get a map of all nodes and link metrics of the entire network
  Find the shortest path on the map from the source node to all destination nodes
Notes: Link state packet – LSP
Mỗi nút tạo ra gói tin cập nhật _ gói tin trạng thái nối kết (link-state packet – LSP), chứa thông tin:
ID của nút đã tạo ra LSP
Một danh sách các nút kề + cost
Một số thứ tự
Time to live của packet

## Slide 7: Link-State Algorithm - Broadcasting
Broadcast of link-state information
  Every node i broadcasts to every other node in the network:
    ID’s of its neighbors: Ni=set of neighbors of i
    Distances to its neighbors: {Cij | j Ni}
  Flooding is a popular method of broadcasting packets
How to limit flooding?
-> Time-to-live

## Slide 8: Building Link State Packets
(a) A subnet. (b) The link state packets for this subnet.
A state packet starts with the ID of the sender, a seq#, age, and a list of neighbors with delay/distance information.

## Slide 9: Unit 03.03.02 CS 5220: COMPUTER COMMUNICATIONS
Dijkstra Algorithm
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 10: Dijkstra Algorithm
Finding the shortest paths from a source node to all other nodes in a network (graph)
More efficient than Bellman-Ford algorithm
Named after scientist Edsger W. Dijkstra

## Slide 11: Dijkstra Algorithm: Idea and Procedure
First iteration
  Finds the closest node from the source node; must be the neighbor of the source node
At the second iteration
  Finds the second closest node from the source node; must be the neighbor of either the source node or the closest node to the source node
At the third iteration
  Finds the third closest node; must be the neighbor of the source node or the first two closest nodes
At the k_th iteration
  Finds the k_th closest node from the source node

## Slide 12: Dijkstra Algorithm: Illustration
s
w"
w"
w'
Closest node to s is 1 hop away
w
x
x'
2nd closest node to s is 1 hop
away from s or w
x
z
z'
3rd closest node to s is 1 hop
away from s, w, or x
W’'
Find shortest paths from source s to all other destinations

## Slide 13: Dijkstra’s algorithm
N: set of nodes for which shortest path already found
Initialization: (Start with source node s)
  N = {s}, Ds = 0, “s is distance zero from itself”
  Dj=Csj for all j  s, distances of directly-connected neighbors
Step A: (Find next closest node i)
  Find i  N such that
  Di = min Dj for j  N
  Add i to N
  If N contains all the nodes, stop
Step B: (update minimum costs)
  For each node j  N
  Dj = min (Dj, Di+Cij)
  Go to Step A
Minimum distance from s to j through node i in N

## Slide 14: Execution of Dijkstra’s algorithm
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
Notes: N: set of nodes for which shortest path already found

## Slide 15: Iteration 1
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3



## Slide 16: Iteration 2
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
2 | {1,2,3} | 3 | 2 | 4 | 7 | 3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3


## Slide 17: Iteration 3
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
2 | {1,2,3} | 3 | 2 | 4 | 7 | 3
3 | {1,2,3,6} | 3 | 2 | 4 | 5 | 3
1
2
4
5
1
1
2
3
2
3
5
2
4
3
3
6


## Slide 18: Iteration 4
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
2 | {1,2,3} | 3 | 2 | 4 | 7 | 3
3 | {1,2,3,6} | 3 | 2 | 4 | 5 | 3
4 | {1,2,3,4,6} | 3 | 2 | 4 | 5 | 3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3


## Slide 19: Iteration 5
Iteration | N | D2 | D3 | D4 | D5 | D6
Initial | {1} | 3 | 2 | 5 |  | 
1 | {1,3} | 3 | 2 | 4 |  | 3
2 | {1,2,3} | 3 | 2 | 4 | 7 | 3
3 | {1,2,3,6} | 3 | 2 | 4 | 5 | 3
4 | {1,2,3,4,6} | 3 | 2 | 4 | 5 | 3
5 | {1,2,3,4,5,6} | 3 | 2 | 4 | 5 | 3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
3


## Slide 20: Shortest-Path Tree from node 1 to other nodes
1
2
4
5
6
1
1
2
3
2
3
5
2
4
3
1
2
4
5
6
1
2
2
3
2
3
3

## Slide 21: Unit 03.03.03 CS 5220: COMPUTER COMMUNICATIONS
Link State Routing, ATM Networks
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 22: Reaction to Failure
In distance vector routing, if a link fails
    Neighboring routers exchange routing tables that may use failed links
In link-state routing, if a link fails,
  Router sets link distance to infinity & floods the network with an update packet
  All routers immediately update their link database & recalculate their shortest paths
  Recovery very quick

## Slide 23: Why is Link State Better?
Fast, loopless convergence
Support for precise metrics, and multiple metrics if necessary (throughput, delay, cost, reliability)
Support for multiple paths to a destination
  algorithm can be modified to find best two paths
Notes: Quá trình đem thông tin vạch đường nhất quán đến mọi nút trong mạng được gọi là sự hội tụ (convergence).

## Slide 24: Problem of Link State Routing
But watch out for old update messages
  Add time stamp or sequence # to each update message
  Check whether each received update message is new
  If new, add it to database and broadcast
  If older, send update message on arriving link
Notes: Một trong những ưu tiên hàng đầu của cơ chế flooding là phải đảm bảo
đem thông tin mới nhất đến mọi nút trong mạng càng nhanh càng tốt (1)
và các thông tin cũ phải được rút ra (2) không cho lưu thông trên mạng nữa.

## Slide 25: Source Routing vs. H-by-H
Source host selects path to be followed by a packet
  Strict: sequence of nodes in path inserted into header
  Loose: subsequence of nodes in path specified
Intermediate switches read next-hop address and remove address
  Or maintained for the reverse path
Source routing allows the host to control the paths that its information traverses in the network
Potentially the means for customers to select what service providers they use

## Slide 26: Example
1
2
3
4
5
6
A
B
Source host
Destination host
1,3,6,B
3,6,B
6,B
B

## Slide 27: Asynchronous Transfer Mode (ATM)
Packet multiplexing and switching
  Fixed-length packets: “cells”
  Connection-oriented
  Rich Quality of Service support
Conceived as end-to-end
  Supporting wide range of services
    Real time voice and video
    Circuit emulation for digital transport
    Data traffic with bandwidth guarantees
Notes: Asynchronous Transfer Mode is a telecommunications standard
defined by ANSI and ITU for digital transmission of multiple types of traffic,
including telephony, data, and video signals in one network without the use of separate overlay networks.

## Slide 28: TDM vs. Packet Multiplexing
 | Variable bit rate | Delay | Burst traffic | Processing
TDM | Multirate only | Low, fixed | Inefficient | Minimal, very high speed
Packet | Easily handled | Variable | Efficient | Header & packet processing required
*In mid-1980s, packet processing mainly in software and hence slow;
By late 1990s, very high speed packet processing possible
Notes: Time-division multiplexing is a method of transmitting and receiving independent signals
over a common signal path by means of synchronized switches at each end of the transmission line
so that each signal appears on the line only a fraction of time in an alternating pattern.

## Slide 29: ATM: Attributes of TDM & Packet Switching
MUX
Wasted bandwidth
ATM
TDM
3 2 1 4 3 2 1 4 3 2 1
4 3 1 3 2 2 1
Voice
Data packets
Images
1
2
3
4
Packet structure gives flexibility & efficiency
Fixed packet length simplifies implementation and makes high speed
Packet Header

## Slide 30: ATM Virtual Connections
Virtual connections setup across network
Connections identified by locally-defined tags
ATM Header contains virtual connection information:
  8-bit Virtual Path Identifier
  16-bit Virtual Channel Identifier
Powerful traffic grooming capabilities
  Multiple VCs can be bundled within a VP
Physical link
Virtual paths
Virtual channels

## Slide 31: MPLS & ATM
ATM initially touted as more scalable than packet switching
Advances in optical transmission proved ATM to be the less scalable: @ 10 Gbps
  Segmentation & reassembly of messages & streams into 48-byte cell payloads difficult & inefficient
  Header must be processed every 53 bytes vs. 500 bytes on average for packets
MPLS (multiprotocol label switching) uses tags to transfer packets across virtual circuits in Internet
  Adopts label switching paradigm, but variable-length packets by packet-over-SONET encapsulation

## Slide 32: Unit 03.03.04 CS 5220: COMPUTER COMMUNICATIONS
RIP and OSPF
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 33: Routing Information Protocol (RIP)
RIP based on routed, distributed in BSD UNIX
Uses the distance-vector algorithm
Runs on top of UDP, port number 520
Metric: number of hops
Max limited to 15
  suitable for small networks (local area environments)
  value of 16 is reserved to represent infinity
  small number limits the count-to-infinity problem

## Slide 34: RIP Operation
Router sends update message to neighbors every 30 sec
A router expects to receive an update message from each of its neighbors within 180 seconds in the worst case
If router does not receive update message from neighbor X within this limit, it assumes the link to X has failed and sets the corresponding minimum cost to 16 (infinity)
Uses split horizon with poisoned reverse
Convergence speeded up by triggered updates
  neighbors notified immediately of changes in distance vector table

## Slide 35: Deficiencies in RIP Protocol
Limited Metric Use
Slow Convergence

## Slide 36: Open Shortest Path First (OSPF)
Fixes some of the deficiencies in RIP
Enables each router to learn complete network topology
Each router monitors the link state to each neighbor and floods the link-state information to other routers
Each router builds an identical link-state database
Allows router to build shortest path tree with router as root
OSPF typically converges faster than RIP when there is a failure in the network
Notes: Open Shortest Path First (OSPF) is a routing protocol for Internet Protocol (IP) networks.
It uses a link state routing (LSR) algorithm and falls into the group of
interior gateway protocols (IGPs), operating within a single autonomous system (AS).

## Slide 37: OSPF Network
To improve scalability, an autonomous system (AS) may be partitioned into two-level areas
  Area defined by 32-bit area ID
  Routers in area only knows complete topology inside area & limits the flooding of link-state information to area
  Area border routers summarize info from other areas
Each area must connect to backbone area (0.0.0.0)
Internal router has all links to nets within the same area
Area border router has links to more than one area
backbone router has links connected to the backbone
Autonomous system boundary (ASB) router has links to another autonomous system

## Slide 38: OSPF Areas
ASB: 4
Area border router : 3, 6, and 8
Internal router: 1,2,7
Backbone router: 3,4,5,6,8
R = router N = network
Area 0.0.0.1
Area 0.0.0.2
Area 0.0.0.3
R1
R2
R4
R5
R7
N1
N2
N3
N4
N5
N6
N7
To another AS
Area 0.0.0.0
R8
R3
R6