## Slide 1: Unit 04.01.01 CS 5220: COMPUTER COMMUNICATIONS
TCP/IP Architecture and IP Packet
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: Why Internetworking?
To build a “network of networks” or internet
  operating over multiple, coexisting, different networks
  providing ubiquitous connectivity through IP packet transfer
  achieving huge economies of scale
G
G
G
G
G
G
H
Net 5
Net 5
H
Net 5
Net 2
H
Net 5
Net 3
H
Net 5
Net 1
Net 5
Net 4

## Slide 3
HTTP
SMTP
RTP
TCP
UDP
IP
Network
Interface 1
Network
Interface 3
Network
Interface 2
DNS
TCP/IP Protocol Suite
(ICMP, ARP)
Best-effort
connectionless packet transfer
Reliable stream service
User
datagram service
Distributed applications

## Slide 4: Encapsulation
TCP Header contains source & destination port numbers
IP Header contains source and destination IP addresses; transport protocol type
Ethernet Header contains source & destination MAC addresses; network protocol type
HTTP Request
TCP header
HTTP Request
IP header
TCP header
HTTP Request
Ethernet header
IP header
TCP header
HTTP Request
FCS

## Slide 5: Internet Addresses
Each host has globally unique logical IP address
Separate address for each physical connection to a network
Routing decision is done based on destination IP address
IP address has two parts:
  netid and hostid
  netid unique, facilitates routing
Dotted Decimal Notation:
  int1.int2.int3.int4
  (intj = jth octet)
  128.100.10.13
DNS resolves IP name to IP address

## Slide 6: Internet Protocol
Provides best effort, connectionless packet delivery
  motivated by need to keep routers simple and by adaptibility to failure of network elements
  packets may be lost, out of order, or even duplicated
  higher layer protocols must deal with these, if necessary
IP also includes:
  Internet Control Message Protocol (ICMP)
  Internet Group Management Protocol (IGMP)

## Slide 7: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Minimum 20 bytes
Up to 40 bytes in options fields

## Slide 8: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Version: current IP version is 4.
Internet header length (IHL): length of the header in 32-bit words.
Type of service (TOS): traditionally priority of packet at each router. Recent Differentiated Services redefines TOS field to include other services besides best effort.

## Slide 9: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Total length: number of bytes of the IP packet including header and data
Identification, Flags, and Fragment Offset: for fragmentation and reassembly.

## Slide 10: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Time to live (TTL): number of hops packet is allowed to traverse in network.
Each router along the path to the destination decrements this value by one.
If the value reaches zero before the packet reaches the destination, the router discards the packet and sends an error message back to the source.

## Slide 11: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Protocol: specifies upper-layer protocol that is to receive IP data at the destination. Examples include TCP (protocol = 6), UDP (protocol = 17), and ICMP (protocol = 1).
Header checksum: verifies the integrity of the IP header.
Source IP address and destination IP address: contain the addresses of the source and destination hosts.

## Slide 12: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Options: Variable length field, allows packet to request special features such as security level, route to be taken by the packet, and timestamp at each router. Detailed descriptions of these options can be found in [RFC 791].
Padding: This field is used to make the header a multiple of 32-bit words.

## Slide 13: IP Header Processing
Compute header checksum for correctness and check that fields in header (e.g. version and total length) contain valid values
Consult routing table to determine next hop
Change fields that require updating (TTL, header checksum)

## Slide 14: Unit 04.01.02 CS 5220: COMPUTER COMMUNICATIONS
IP Addressing
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 15: IP Addressing
Each host on Internet has unique 32 bit IP address
Each address has two parts: netid and hostid
netid is unique & administered by Internet registration
netid facilitates routing and reduces routing table
A separate address is required for each physical connection of a host to a network; “multi-homed” hosts
Dotted-Decimal Notation:
  int1.int2.int3.int4 where intj = integer value of jth octet
  IP address of 10000000 10000111 01000100 00000101
  is 128.135.68.5 in dotted-decimal notation

## Slide 16: Classful Addresses
0
1
0
netid
netid
hostid
hostid
7 bits
24 bits
14 bits
16 bits
Class A
Class B
126 networks with up to 16 million hosts
16,382 networks with up to 64,000 hosts
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
1
1
netid
hostid
21 bits
8 bits
Class C
0
2 million networks with up to 254 hosts
192.0.0.0 to
223.255.255.255

## Slide 17: Class D Addresses
Up to 250 million multicast groups at the same time
Permanent group addresses
  All systems in LAN; All routers in LAN;
  All OSPF routers on LAN; All designated OSPF routers on a LAN, etc.
Temporary groups addresses created as needed
Special multicast routers
1
1
multicast address
28 bits
1
0
Class D
224.0.0.0 to
239.255.255.255

## Slide 18: Reserved Host IDs (all 0s & 1s)
Broadcast address has hostid set to all 1s
0
0
0
0
0
0
this host
(used when
booting up)
0
0
0
host
a host
in this
network
1
1
1
1
1
1
broadcast on local network
1
1
1
1
1
1
1
netid
broadcast on distant network
Internet address used to refer to network has hostid set to all 0s

## Slide 19: Private IP Addresses
Specific ranges of IP addresses set aside for use in private networks (RFC 1918)
Use restricted to private internets; routers in public Internet discard packets with these addresses
Range 1: 10.0.0.0 to 10.255.255.255
Range 2: 172.16.0.0 to 172.31.255.255
Range 3: 192.168.0.0 to 192.168.255.255
Network Address Translation (NAT) used to convert between private & global IP addresses

## Slide 20: Example of IP Addressing
R
Network
128.135.0.0
Network
128.140.0.0
H
H
H
H
H
R = router
H = host
Interface
Address is
128.135.10.2
Interface
Address is
128.140.5.35
128.135.10.20
128.135.10.21
128.135.40.1
128.140.5.36
128.140.5.40
Address with host ID=all 0s refers to the network
Address with host ID=all 1s refers to a broadcast packet
What class types?

## Slide 21: Subnets
A campus network consisting of LANs for various departments.
- How to allow a network to be split into several parts for internal use but still act like a single network to the outside

## Slide 22: Unit 04.01.03 CS 5220: COMPUTER COMMUNICATIONS
Subnetting
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 23: Subnet Addressing
Subnet addressing introduces another hierarchical level
Transparent to remote networks
Simplifies management of multiplicity of LANs
Masking used to find subnet number

## Slide 24: Subnetting Scheme
Organization has Class B address (16 host ID bits) with network ID: 150.100.0.0
Create subnets with up to 100 hosts each
  7 bits sufficient for each subnet (IP mask 7 bits)
  16-7 = 9 bits for subnet ID (2^9 – 2 = 510 subnets)
Apply subnet mask to IP addresses to find corresponding subnet
  Example: Find subnet for 150.100.12.176
  IP address = 10010110 01100100 00001100 10110000
  Mask = 11111111 11111111 11111111 10000000 (7 0s)
  AND = 10010110 01100100 00001100 10000000
  Subnet = 150.100.12.128
  Subnet address used by routers within organization

## Slide 25: Subnet Range
  Given the subnet 150.100.12.128
  IP address 150.100.12.128 is used to identify the subnetwork
  IP address 150.100.12.255 is used to broadcast packets in the subnet
  Range of the subnet IP address is between
  IP address = 10010110 01100100 00001100 10000001
  to
  IP address = 10010110 01100100 00001100 11111110
  That is, 150.100.12.129 to 150.100.12.254

## Slide 26: Unit 04.01.04 CS 5220: COMPUTER COMMUNICATIONS
Subnet Routing Examples
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 27: Routing Table
Each row in routing table contains:
  Destination IP address
  IP address of next-hop router
  Physical address
  Statistics information
  Flags
    H=1 (0) indicates route is to a host (network)
    G=1 (0) indicates route is to a router (directly connected destination)

## Slide 28: Routing Search and Actions
Routing table search order & action
  Complete destination address; send as per next-hop & G flag
  Destination network ID; send as per next-hop & G flag
  Default router entry; send as per next-hop
  Declare packet undeliverable; send ICMP “host unreachable error” packet to originating host

## Slide 29: Example 1: A packet with 150.100.15.11 arrives at R1
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
150.100.15.11
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
150.100.12.128 150.100.12.129 emd0
150.100.12.0 150.100.12.4 emd1
150.100.15.0 150.100.12.1 G emd1
Routing Table at R1

## Slide 30: Example 1: Subnetting Scheme
IP address 150.100.15.11 in binary string is
10010110 01100100 00001111 00001011
Apply subnet mask to IP addresses to find corresponding subnet
  IP address = 10010110 01100100 00001111 00001011
  Mask = 11111111 11111111 11111111 10000000
  AND = 10110110 01100100 00001111 00000000
  Subnet = 150.100.15.0

## Slide 31
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
150.100.12.128 150.100.12.129 emd0
150.100.12.0 150.100.12.4 emd1
150.100.15.0 150.100.12.1 G emd1
Routing Table at R1
150.100.15.11

## Slide 32: Example 2: Host H5 sends packet to host H2
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
default 150.100.15.54 G emd0
150.100.15.0 150.100.15.11 emd0
Routing Table at H5

## Slide 33: Example 2: Host H5 sends packet to host H2
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
default 150.100.15.54 G emd0
150.100.15.0 150.100.15.11 emd0
Routing Table at H5
150.100.12.176

## Slide 34: Example: Host H5 sends packet to host H2
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
default 150.100.12.4 G emd0
150.100.15.0 150.100.15.54 emd1
150.100.12.0 150.100.12.1 emd0
Routing Table at R2
150.100.12.176

## Slide 35
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4
Destination Next-Hop Flags Net I/F
127.0.0.1 127.0.0.1 H lo0
150.100.12.128 150.100.12.129 emd0
150.100.12.0 150.100.12.4 emd1
150.100.15.0 150.100.12.1 G emd1
Routing Table at R1
150.100.12.176

## Slide 36: Subnet Example
R1
H1
H2
H3
H4
R2
H5
To the rest of
the Internet
150.100.0.1
150.100.12.128
150.100.12.0
150.100.12.176
150.100.12.154
150.100.12.24
150.100.12.55
150.100.12.1
150.100.15.54
150.100.15.0
150.100.15.11
150.100.12.129
150.100.12.4

## Slide 37: Routing with Subnetworks
IP layer in hosts and routers maintain a routing table
Originating host: To send an IP packet, consult routing table
  If destination host is in same network, send packet directly using appropriate network interface
  Otherwise, send packet indirectly; typically, routing table indicates a default router
Router: Examine IP destination address in arriving packet
  If destination IP address not own, router consults routing table to determine next-hop and associated network interface & forwards packet