## Slide 1: Unit 04.02.01 CS 5220: COMPUTER COMMUNICATIONS
Classless Interdomain Routing (CIDR)
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 2: IP Address Problems
IP Address Exhaustion
  Class A, B, and C address structure inefficient
    Class B too large for most organizations, but future proof
    Class C too small
IP routing table size
  Growth in # of networks in Internet reflected in # of table entries
    Stress on router processing power and memory allocation
Short-term solution:
  Classless Interdomain Routing (CIDR), RFC 1518
  New allocation policy (RFC 2050)
  Private IP Addresses set aside for intranets (NAT)
Long-term: IPv6 with much bigger address space

## Slide 3: Classless Interdomain Routing Scheme
CIDR uses an arbitrary prefix length to indicate the network number
  205.100.0.0/22
  /22 means mask: 11111111 11111111 11111100 00000000
  255.255.252.0
Packets are routed according to the prefix w/o address classes
  An entry in CIDR routing table contains 32-bit IP address and 32-bit mask
Enables supernetting to allow a single routing entry to cover a block of classful addresses

## Slide 4: CIDR Aggregation
A company is allocated the following four contiguous /24 networks. At some router, it is often true that all of the four networks use the same outgoing line. CIDR aggregation can be done to reduce the number of entry at the router.
    128.56.24.0/24; 10000000 00111000 00011000 00000000
    128.56.25.0/24; 10000000 00111000 00011001 00000000
    128.56.26.0/24; 10000000 00111000 00011010 00000000
    128.56.27.0/24. 10000000 00111000 00011011 00000000
    By Per-bit AND
    128.56.24.0/22 10000000 00111000 00011000 00000000
    (Instead of 4 entries in routing table, one entry is sufficient by CIDR)

## Slide 5: CIDR Scheme and Range
CIDR deals with Routing Table Explosion Problem
  Networks represented by prefix and mask
  Summarize a contiguous group of class C addresses using variable-length mask, if all of them use the same outgoing line
Solution: Route according to prefix of address, not class
  Routing table entry has <IP address, network mask>
  Example: 192.32.136.0/21
  11000000 00100000 10001000 00000001 min address
  11111111 11111111 11111--- -------- mask
  11000000 00100000 10001--- -------- IP prefix
  11000000 00100000 10001111 11111110 max address
  Eight C networks: 192.32.136.0/24 to 192.32.143.0/24

## Slide 6: CIDR Supernetting Example (1)
Summarize a contiguous group of class C addresses using variable-length mask
Example: 150.158.16.0/20
  IP Address (150.158.16.0) & mask length (20)
  IP address = 10010110 10011110 00010000 00000000
  Mask = 11111111 11111111 11110000 00000000
  Contains 16 Class C blocks:
  From 10010110 10011110 00010000 00000000
  i.e. 150.158.16.0/24
  Up to 10010110 10011110 00011111 00000000
  i.e. 150.158.31.0/24

## Slide 7: CIDR Supernetting Example (2)
A router has the following CIDR entries in its routing table:
Address/mask Next hop
    128.56.24.0/22 Interface 0
    128.56.60.0/22 Interface 1
    default Router 2
A packet comes with IP address of 128.56.63.10. What does the router do?

## Slide 8: CIDR Supernetting Example (2) – Cont.
128.56.63.10 and mask 22 bits
  IP address = 10000000 00111000 01111111 00001010
  Mask = 11111111 11111111 11111100 00000000
  By Per-bit AND
  Prefix = 10000000 00111000 01111100 00001010
  i.e. 128.56.60
  Router table lookup and match, should go to interface 1

## Slide 9: New Address Allocation Policy
Class A & B assigned only for clearly demonstrated need
Consecutive blocks of class C assigned (up to 64 blocks)
  All IP addresses in the range have a common prefix, and every address with that prefix is within the range
  Arbitrary prefix length for network ID improves efficiency
Address assignment should reflect the physical topology of the network
  Facilitates the aggregation of logical packet flows into physical flows
Address Requirement | Address Allocation
< 256 | 1 Class C
256<,<512 | 2 Class C
512<,<1024 | 4 Class C
1024<,<2048 | 8 Class C
2048<,<4096 | 16 Class C
4096<,<8192 | 32 Class C
8192<,<16384 | 64 Class C

## Slide 10: Longest Prefix Match
By CIDR, multiple entries may match a given IP destination address but different prefix
Example: perform CIDR on the following three /24 IP addresses (but 128.56.24.0/24 to a different port)
  128.56.25.0/24;
  128.56.26.0/24;
  128.56.27.0/24;
  By CIDR aggregation: 128.56.24.0/22
  What if a packet with destination IP address 128.56.24.1 comes?

## Slide 11: Example of Longest Prefix Match
R
Company B
128.56.24.0/24
Company A
128.56.25.0/24
128.56.26.0/24
128.56.27.0/24
Packet coming with
Address 128.56.24.1
Port 0
Port 1
Address/mask Next Hop
128.56.24.0/24 0
128.56.24.0/22 1
Routing Table at R
Longest Prefix Match: packet must be routed using the more specific route (128.56.24.0/24)

## Slide 12: Unit 04.02.02 CS 5220: COMPUTER COMMUNICATIONS
ARP, Fragmentation and Reassembly
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 13: Address Resolution Protocol
IP addresses are said to be logical, because they are defined in terms of logical topology of the routers and end systems.
The logical IP addresses need to be converted into specific physical addresses that identify the physical endpoints for the Ethernet sender and receiver
ARP: conversion between IP address and Physical address

## Slide 14: Address Resolution Protocol (ARP)
H1
H2
H3
H4
H1
H2
H3
H4
ARP request (what is the MAC address of 150.100.76.22?)
ARP response (my MAC address is 08:00:5a:3b:94)
150.100.76.20
150.100.76.21
150.100.76.22
150.100.76.23
How to map an IP address to a physical address? How to speed up? How fresh?
H1 wants to learn physical address of H3 -> broadcasts an ARP request
Every host receives the request, but only H3 reply with its physical address

## Slide 15: Fragmentation and Reassembly
IP
IP
Router
Source
Destination
Network
Network
Fragment
at source
Fragment
at router
Reassemble
at destination
Q1: who does it?
Q2: penalty?
Each physical network imposes a certain packet size limitation on the packet to be carried, called maximum transmission unit MTU.

## Slide 16: RE: IP Packet Header
Version IHL Type of Service Total Length
Identification Flags Fragment Offset
Time to Live Protocol Header Checksum
Source IP Address
Destination IP Address
Options Padding
0 4 8 16 19 24 31
Identification, Flags, and Fragment Offset: used for fragmentation and reassembly
Fragment offset is 13 bits; total length is 16 bits, what does it imply?

## Slide 17: Example: Fragmenting a Packet
Packet is to be forwarded to a network with MTU of 576 bytes. The packet has an IP header of 20 bytes and a data part of 1484 bytes.
Maximum data length per fragment = 576 - 20 = 556 bytes.
Set maximum data length to 552 bytes to get multiple of 8.
 | Total Length | Id | MF | Fragment Offset
Original packet | 1504 | x | 0 | 0
Fragment 1 | 572 | x | 1 | 0
Fragment 2 | 572 | x | 1 | 69
Fragment 3 | 400 | x | 0 | 138

## Slide 18: Unit 04.02.03 CS 5220: COMPUTER COMMUNICATIONS
DHCP, NAT
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 19: DHCP
Dynamic Host Configuration Protocol (RFC 2131)
Bootstrap Protocol BOOTP allows a diskless workstation to be remotely booted up in a network
  UDP port 67 (server) & port 68 (client)
DHCP builds on BOOTP to allow servers to deliver configuration information to a host
  Used extensively to assign temporary IP addresses to hosts
  Allows ISP to maximize usage of their limited IP addresses
  Time thresholds to enforce lease time

## Slide 20: Network Address Translation (NAT)
Class A, B, and C addresses have been set aside for use within private Internets
  Private IP addresses are sufficient for use inside of private networks
  But packets with private (“unregistered”) addresses are discarded by routers in the global Internet
NAT (RFC 1631): method for mapping packets from hosts in private internets into packets that can traverse the Internet
  A device (computer, router, firewall) acts as an agent between a private network and a public network
  A number of hosts can share a limited number of registered IP addresses

## Slide 21: Placement of Operation of a NAT Box
NAT: provides mapping between public IP address and private IP addresses

## Slide 22: NAT Operations
Hosts inside private networks generate packets with private IP address & TCP/UDP port #s
NAT maps each private IP address & port # into shared global IP address & available port #
Translation table allows packets to be routed unambiguously
NAT Device
Private Network
Public Network
192.168.0.13;w
192.168.0.10;x
Address Translation Table: 192.168.0.10; x 128.100.10.15; y
192.168.0.13; w 128.100.10.15; z
128.100.10.15;y
128.100.10.15; z

## Slide 23: NAT Discussions
In theory, up to 2^16 private IP addresses supported by a single public IP address in NAT box
Overhead in NAT operation
TCP/UDP Port number used for NAT mapping at IP layer, violating OSI layer architecture principle

## Slide 24: Unit 04.02.04 CS 5220: COMPUTER COMMUNICATIONS
IPv6
XIAOBO ZHOU, Ph.D.
Professor, Department of Computer Science

## Slide 25: IPv6
Longer address field:
  128 bits can support up to 3.4 x 1038 hosts
Simplified header format:
  Simpler format to speed up processing of each packet header
  All fields are of fixed size

## Slide 26: IPv4 vs IPv6 Overview
  IPv4 vs IPv6 fields:
    Same: Version
    Dropped: Header length, ID/flags/frag offset, header checksum
    Replaced:
      Datagram length by Payload length
      Protocol type by Next header
      TTL by Hop limit
      TOS by traffic class
    New: Flow label

## Slide 27: IPv6 Header Format
Version field same size, same location
Traffic class to support differentiated services
Flow: sequence of packets from particular source to particular destination for which source requires special handling
Version Traffic Class
Flow Label
Payload Length Next Header Hop Limit
Source Address
Destination Address
0 4 12 16 24 31

## Slide 28: IPv6 Basic Header Format
Payload length: length of data excluding header, up to 65535 B
Next header: type of extension header that follows basic header
Hop limit: # hops packet can travel before being dropped by a router
Version Traffic Class
Flow Label
Payload Length Next Header Hop Limit
Source Address
Destination Address
0 4 12 16 24 31

## Slide 29: Extension Headers
Allows an arbitrary number of extension headers be placed between the basic header and the payload (the extension headers are chained by the next header field)
Large Packet (Jumbo packet): payload>64K
Next header 0
194
Opt len = 4
Jumbo payload length
0 8 16 24 31

## Slide 30: Extension Headers
Next header Reserved Fragment offset Res M
Identification
0 8 16 29 31
  Fragmentation: At source only
  Source performs “path MTU discovery” (a fragment extension header for each packet fragment)

## Slide 31: Extension Headers
Source Routing: strict/loose routes
Reserved Strict/loose bit mask
Address 1
Address 2
0 8 16 24 31
Next header Header length Routing type = 0 Segment left
. . .
Address 24

## Slide 32: IPv6 Addressing
Address Categories
  Unicast: single network interface
  Multicast: group of network interfaces, typically at different locations. Packet sent to all.
  Anycast: group of network interfaces. Packet sent to only one interface in group, e.g. nearest.
Hexadecimal notation
  Groups of 16 bits represented by 4 hex digits
  Separated by colons
    4BF5:AA12:0216:FEBC:BA5F:039A:BE9A:2176
  Shortened forms:
    4BF5:0000:0000:0000:BA5F:039A:000A:2176
    To 4BF5:0:0:0:BA5F:39A:A:2176
    To 4BF5::BA5F:39A:A:2176
  Mixed notation:
    ::FFFF:128.155.12.198

## Slide 33: Migration from IPv4 to IPv6
Gradual transition from IPv4 to IPv6
Dual IP stacks: routers run IPv4 & IPv6
  Type field used to direct packet to IP version
IPv6 islands can tunnel across IPv4 networks
  Encapsulate user packet insider IPv4 packet
Source
Destination
IPv6 network
IPv4 network
IPv6 network
Tunnel
Tunnel head-end
Tunnel tail-end
IPv6 header
IPv4 header