## Slide 1
Non-uniform memory access
OSG202 Presentation
Chapter 8. Multiple processor systems
OSG202 Presentation
NUMA
Name
ID
Class
Nguyen Dang Loc
SE160199
SE1602

## Slide 2
Agenda
01
Basic concepts
02
03
Some basic related concepts in multiprocessors
What’s NUMA?
More detail information and characteristics of NUMA
Assessment
Comparison with UMA;
pros & cons, its applications

## Slide 3
3 models
Uniform Memory Access (UMA)
Non-uniform Memory Access (NUMA)
Cache-only Memory Access (COMA)
Basic concepts
Multiprocessor
A computer system with two or more CPUs share full access to a common RAM.
Boost the system’s execution speed
Shared-memory multiprocessor
Distributed memory multiprocessor
Property
Every CPU can address all of memory.
UMA (Uniform Memory Access)
NUMA (Non-uniform Memory Access)
Bus-based UMA (SMP)
shared-memory
Identical memory access latencies for any processor
Potential overload and becomes a performance bottleneck
!
Single memory, accessed by all the processors
Bus-based, crossbar switch, multistage switching network
Performance will be limited
by this memory organization!
Each processor connected with the dedicated memory.
Logically follow in scaling from SMP architectures.
Increase the available bandwidth to the memory

## Slide 4
What’s NUMA?
Definition
NUMA is a method of configuring a cluster of microprocessor in a multiprocessing system.
Key characteristics
There is a single address space visible to all CPUs.
Access to remote memory via LOAD/STORE instructions.
Access local memory faster than remote memory.
Vary memory access latencies
A Node
Model of NUMA system
Node of a NUMA machine
UMA region – as a node.
Node contains processors, bus,
physical memory.
Each core has a memory controller.
NUMA machine
Multiple nodes are combined to form a NUMA machine.
Link together via a fast interconnect.
Drawbacks
Performance of application depends on the number of nodes.
Design goal
Ideal system
Make the routers as fast as possible, minimize the difference between local and remote memory references.
Perfect (infinite) memory bandwidth
Perfect (single-cycle) memory latency

## Slide 5
Cluster computing
A "cluster in a box"
Maintain hierarchical view of the data on all the nodes.
Problems
Cache - coherent NUMA
NUMA as a tightly-coupled form of cluster computing.
Data is moved on the bus between the clusters of a NUMA system using scalable coherent interface (SCI) technology.
Reduce the latency
Caches are used
Keeping cached copies of data coheren
Non Cache-coherent NUMA
→ Simpler model, complex to program
Cache-coherent NUMA
→ Enhance locality, easier programming
Benefits
Migration: lower latency + more bandwidth
Replication: data being replicated to reduce latency + contention
Solutions
Complex structure
Significant overhead
Keep a consistent memory image
Allocate processors and memory in NUMA-friendly ways
SCI define a directory-based cache coherency protocol - avoid scalability limitations

## Slide 6
Assessment
Comparison with UMA
Advantages
Disadvantages
Applications
BASIS | UMA | NUMA
Basic | Single memory controller | Multiple memory controller
Bus type | Single, multiple and crossbar | Tree and hierarchical
Memory access latencies | Equal | Changes according to the distance of microprocessor
Suitable for | General-purpose & time-sharing applications | Real-time & time-critical applications
Speed | Slower | Faster
Bandwidth | Limited | More than UMA
NUMA has improved the performance as compared to UMA architecture.
Conclusion
Faster movement of data, less replication, easier programming.
Share memory locally.
Improving performance and ability of the system is expanded.
Interconnect
M0
M1
M2
M3
P3
P2
P1
P0
Long
latency
UMA
Interconnect
P0
P1
P2
P3
M3
M2
M1
M0
Long
latency
Short
latency
NUMA
If many remote node accesses, performance begins to break down.
Synchronization
Memory Consistency
More complex hardware is needed.
Data mining
Database
Virtual machine
Pthreads

## Slide 7
Example
AMD64 Opteron
Compare to Intel chip-set
Processors are connected with high- speed HyperTransport.
The Opteron CPU directly supports up to an 8-way configuration.
As of 2011, CC-NUMA systems are multiprocessor systems based on the AMD Opteron processor.
The Opteron architecture has demonstrated better multi-processor scaling than the Intel Xeon.
Intel migrated to a memory architecture similar to the Opteron's for Intel Core i7 family of processors and their Xeon derivatives.

## Slide 8
References
Computer Science 246 slides, Prof. David Brooks (2010)
[2]
Non-uniform memory access - wikipedia.org
[3]
Non-uniform memory access, Bruce Jacon (2008) - sciencedirect.com
[4]
Shared memory vs. Distributed memory (2016) - stackoverflow.com
[5]
Difference between UMA & NUMA (2019) - geeksforgeeks.org
[6]
[1]
Modern Operating System ebook, Tanenbaum 4th edition, Chap 8.1
NUMA pros & cons - faadooengineers.com
[7]

## Slide 9
OSG202 Presentation
OSG202 Presentation
Name
ID
Class
Nguyen Dang Loc
SE160199
SE1602
Thank you!
Goodbye!